## Slide 1: Network Introduction
wangth (2018-2023, CC BY-SA)
? (2009-2017)

## Slide 2: TCP/IP and the Internet
In 1969
  ARPA funded and created the “ARPANet” network
    美國高等研究計劃署 (ARPA: Advanced Research Project Agency)
    NCP – Network Control Protocol
      Allow an exchange of information between separated computers
In 1973
  How to connect ARPANet with SATNet and ALOHANet
  TCP/IP begun to be developed
In 1983
  TCP/IP protocols replaced NCP as the ARPANet’s principal protocol
  ARPANet  MILNet + ARPANet = Internet
In 1985
  The NSF created the NSFNet to connect to Internet
In 1990
  ARPANet passed out of existence, and in 1995, the NSFNet became the primary Internet backbone network
NSF: National Science Foundation

## Slide 3: Introduction – ARPANet
https://inventiontourblog.wordpress.com/2015/03/31/internet-advanced-research-project-agency-arpa-develops-the-first-computer-network/
Stanford Research Institute
UC Santa Barbara
University of Utah
UCLA

## Slide 4: Introduction – Why TCP/IP ?
The gap between applications and Network
  Network
    802.3 Ethernet
    802.4 Token bus
    802.5 Token Ring
    802.11 Wireless
    802.16 WiMAX
  Application
    Reliable
    Performance
Applications
Libraries
Linux kernel
High-level abstractions
Low-level interfaces
File-systems
Network protocols
Hardware
We need something to do the translating work!
TCP/IP it is!!

## Slide 5: Introduction – Layers of TCP/IP (1)
TCP/IP is a suite of networking protocols
  4-layer architecture
    Link layer (data-link layer)
      Include device drivers to handle hardware details
    Network layer (IP)
      Handle the movement of packets around the network
    Transport layer (Port)
      Handle flow of data between hosts
    Application

## Slide 6: Introduction – Layers of TCP/IP (2)
Each layer has several protocols
  A layer define a data communication function that may be performed by certain protocols
  A protocol provides a service suitable to the function of that layer
User Process
User Process
User Process
User Process
TCP
UDP
ICMP
IP
IGMP
ICMP
IP
IGMP
Application
transport
network
link
media

## Slide 7: Introduction – Layers of TCP/IP (2)
ISO/OSI Model (International Organization for Standardization / Open System Interconnection Reference Model)
TCP/IP Model
Application
Presentation
Session
Transport
Network
Data-link
Physical
Application
Transport
Internet
Network Interface
OSI Model
TCP/IP
TCP/IP and the OSI model

## Slide 8: Introduction
TCP/IP
  Used to provide data communication between hosts
    How to delivery data reliably
    How to address remote host on the network
    How to handle different type of hardware device

## Slide 9: Introduction – Addressing
Addressing
  MAC Address
    Media Access Control Address
    48-bit Network Interface Card Hardware Address
      24-bit manufacture ID
      24-bit serial number
    Ex:
      00:07:e9:10:e6:6b
  IP Address
    32-bit Internet Address (IPv4)
    Ex:
      140.113.209.64
  Port
    16-bit uniquely identify application (1 ~ 65536)
    Ex:
      FTP port 21, SSH port 22, Telnet port 23

## Slide 10: Link Layer

## Slide 11: Link Layer – Introduction of Link Layer
Purpose of the link layer
  Send and receive IP datagram for IP module
  ARP request and reply
  RARP request and reply
TCP/IP support various link layers, depending on the type of hardware used:
  Ethernet
    Teach in this class
  Token Ring
  FDDI (Fiber Distributed Data Interface)
  Serial Line

## Slide 12: Link Layer – Ethernet
Features
  Predominant form of local LAN technology used today
  Use CSMA/CD
    Carrier Sense, Multiple Access with Collision Detection
  Use 48-bit MAC address
  Operate at 10 Mbps
    Fast Ethernet at 100 Mbps
    Gigabit Ethernet at 1000 Mbps
    10 Gigabit Ethernet at 10,000 Mbps (10Gbps)
  Ethernet frame format is defined in RFC 894
    This is the actually used format in reality

## Slide 13: Link Layer – Ethernet Frame Format
48-bit hardware address
  For both destination and source address
16-bit type is used to specify the type of following data
  0800  IP datagram
  0806  ARP, 8035  RARP
destination
addr
source
addr
type
data
CRC
6
6
2
46-1500
type 0800
IP datagram
2
46-1500
type 0806
ARP request/reply
2
28
PAD
18
type 0835
RARP request/reply
2
28
PAD
18
Ethernet Encapsulation(RFC 894)
46-1500 byte

## Slide 14: Link Layer – Loopback Interface
Pseudo NIC
  Allow client and server on the same host to communicate with each other using TCP/IP
  IP
    127.0.0.1
  Hostname
    localhost
IP output
function
IP input
function
place on IP input queue
place on IP input queue
destination IP address equal broadcast address or multicast address?
destination IP address equal interface IP address?
demultiplex based on Ethernet frame type
ARP
loopback driver
Yes
Yes
No
Send
Receive
Ethernet
No, use ARP to get destination Ethernet address
Ethernet driver
IP
ARP

## Slide 15: Link Layer – MTU
Maximum Transmission Unit
  Limit size of payload part of Ethernet frame
    1500 bytes
  If the IP datagram is larger than MTU,
    IP performs “fragmentation”
MTU of various physical device
Path MTU
  Smallest MTU of any data link MTU between the two hosts
  Depend on route
Network | MTU (bytes)
Hyperchannel | 65536
16 Mbits/sec token ring (IMB) | 17914
4 Mbits/sec token ring (IEEE 802.5) | 4464
FDDI | 4352
Ethernet | 1500
IEEE 802.3/802.2 | 1492
X.25 | 576
Point-to-point (low delay) | 296

## Slide 16: Link Layer – MTU
To get MTU info
$ ifconfig
em0: flags=8843<UP,BROADCAST,RUNNING,SIMPLEX,MULTICAST> mtu 9000
options=b<RXCSUM,TXCSUM,VLAN_MTU>
inet 192.168.7.1 netmask 0xffffff00 broadcast 192.168.7.255
ether 00:0e:0c:01:d7:c8
media: Ethernet autoselect (1000baseTX <full-duplex>)
status: active
fxp0: flags=8843<UP,BROADCAST,RUNNING,SIMPLEX,MULTICAST> mtu 1500
options=b<RXCSUM,TXCSUM,VLAN_MTU>
inet 140.113.17.24 netmask 0xffffff00 broadcast 140.113.17.255
ether 00:02:b3:99:3e:71
media: Ethernet autoselect (100baseTX <full-duplex>)
status: active

## Slide 17: Network Layer

## Slide 18: Network Layer – Introduction to Network Layer
Unreliable and connectionless datagram delivery service
  IP Routing
  IP provides best effort service (unreliable)
  IP datagram can be delivered out of order (connectionless)
Protocols using IP
  TCP, UDP, ICMP, IGMP

## Slide 19: Network Layer – IP Header
20 bytes in total length, except options
4-bit version
4-bit header length
8-bit type of service (TOS)
16-bit total length (in bytes)
16-bit identification
3-bit flags
13-bit fragment offset
32-bit source IP address
32-bit destination IP address
options (if any)
data
8-bit time to live (TTL)
8-bit protocol
16-bit header checksum
0
15 16
31
20 bytes

## Slide 20: The Network Layer – IP Address
32-bit long
  Network part
    Identify a logical network
  Host part
    Identify a machine on certain network
IP address category
E.g.,
  NCTU
    Class B address: 140.113.0.0
    Network ID: 140.113
    Number of hosts: 256*256 = 65536
Class | 1st byte | Format | Comments
A | 1-126 | N.H.H.H | Very early networks, or reserved for DOD
B | 128-191 | N.N.H.H | Large sites, usually subnetted, were to get
C | 192-223 | N.N.N.H | Easy to get, often obtained in sets
D | 224-239 | - | Multicast addresses, not permanently assigned
E | 240-254 | - | Experimental addresses

## Slide 21: Network Layer – Subnetting, CIDR, and Netmask (1)
Problems of Class A or B network
  Number of hosts is enormous
  Hard to maintain and management
  Solution => Subnetting
Problems of Class C network
  255*255*255 number of Class C network make the size of Internet routes huge
  Solution => Classless Inter-Domain Routing

## Slide 22: Network Layer – Subnetting, CIDR, and Netmask (2)
Subnetting
  Borrow some bits from network ID to extends hosts ID
  E.g.,
    Class B address : 140.113.0.0
= 256 Class C-like IP addresses
in N.N.N.H subnetting method
    140.113.209.0 subnet
Benefits of subnetting
  Reduce the routing table size of Internet routers
  Ex:
    All external routers have only one entry for 140.113 Class B network

## Slide 23: Network Layer – Subnetting, CIDR, and Netmask (3)
Netmask
  Specify how many bits of network-ID are used for network-ID
  Continuous 1 bits form the network part
  E.g.,
    255.255.255.0 in NCTU-CS example
      256 hosts available
    255.255.255.248 in ADSL example
      Only 8 hosts available
  Shorthand notation
    Address/prefix-length
      Ex: 140.113.209.8/24

## Slide 24: Network Layer – Subnetting, CIDR, and Netmask (4)
How to determine your network ID?
  Bitwise-AND IP and netmask
  E.g.,
  140.113.214.37 & 255.255.255.0 => 140.113.214.0
  140.113.209.37 & 255.255.255.0 => 140.113.209.0
  140.113.214.37 & 255.255.0.0 => 140.113.0.0
  140.113.209.37 & 255.255.0.0 => 140.113.0.0
  211.23.188.78 & 255.255.255.248 => 211.23.188.72
    78 = 01001110
    78 & 248 = 01001110 & 11111000 = 72

## Slide 25: Network Layer – Subnetting, CIDR, and Netmask (5)
In a subnet, not all IP are available
The first one IP  network ID
The last one IP  broadcast address
E.g.,
Netmask 255.255.255.0
140.113.209.32/24
140.113.209.0 => network ID
140.113.209.255 => broadcast address
1 ~ 254, total 254 IPs are usable
Netmask 255.255.255.252
211.23.188.78/29
211.23.188.72 => network ID
211.23.188.79 => broadcast address
73 ~ 78, total 6 IPs are usable

## Slide 26: Network Layer – Subnetting, CIDR, and Netmask (6)
The smallest subnetting
  Network portion : 30 bits
  Host portion : 2 bits
=> 4 hosts, but only 2 IPs are available
ipcalc
  $ pkg install ipcalc
  /usr/ports/net-mgmt/ipcalc
$ ipcalc 140.113.235.100/28
Address: 140.113.235.100 10001100.01110001.11101011.0110 0100
Netmask: 255.255.255.240 = 28 11111111.11111111.11111111.1111 0000
Wildcard: 0.0.0.15 00000000.00000000.00000000.0000 1111
=>
Network: 140.113.235.96/28 10001100.01110001.11101011.0110 0000
HostMin: 140.113.235.97 10001100.01110001.11101011.0110 0001
HostMax: 140.113.235.110 10001100.01110001.11101011.0110 1110
Broadcast: 140.113.235.111 10001100.01110001.11101011.0110 1111
Hosts/Net: 14 Class B

## Slide 27: Network Layer – Subnetting, CIDR, and Netmask (7)
Network configuration for various lengths of netmask
Length | Host bits | Hosts/net | Dec. netmask | Hex netmask
/20 | 12 | 4094 | 255.255.240.0 | 0xFFFFF000
/21 | 11 | 2046 | 255.255.248.0 | 0xFFFFF800
/22 | 10 | 1022 | 255.255.252.0 | 0xFFFFFC00
/23 | 9 | 510 | 255.255.254.0 | 0xFFFFFE00
/24 | 8 | 254 | 255.255.255.0 | 0xFFFFFF00
/25 | 7 | 126 | 255.255.255.128 | 0xFFFFFF80
/26 | 6 | 62 | 255.255.255.192 | 0xFFFFFFC0
/27 | 5 | 30 | 255.255.255.224 | 0xFFFFFFE0
/28 | 4 | 14 | 255.255.255.240 | 0xFFFFFFF0
/29 | 3 | 6 | 255.255.255.248 | 0xFFFFFFF8
/30 | 2 | 2 | 255.255.255.252 | 0xFFFFFFFC

## Slide 28: Network Layer – Subnetting, CIDR, and Netmask (8)
CIDR (Classless Inter-Domain Routing)
  Use address mask instead of old address classes to determine the destination network
  CIDR requires modifications to routers and routing protocols
    Need to transmit both destination address and mask
  Ex:
    We can merge two Class C network: 203.19.68.0/24, 203.19.69.0/24 => 203.19.68.0/23
  Benefit of CIDR
    We can allocate continuous Class C network to organization
      Reflect physical network topology
      Reduce the size of routing table

## Slide 29: Network Layer – IP Routing (1)
Difference between Host and Router
  Router forwards datagram from one of its interface to another, while host does not
  Almost every Unix system can be configured to act as a router or both
    net.inet.ip.forwarding=1
Router
  IP layer has a routing table, which is used to store the information for forwarding datagram
  When router receiving a datagram
    If Dst. IP = my IP, demultiplex to other protocol
    Other, forward the IP based on routing table

## Slide 30: Network Layer – IP Routing (2)
Routing table information
  Destination IP
  IP address of next-hop router or IP address of a directly connected network
  Flags
  Next interface
IP routing
  Done on a hop-by-hop basis
  It assumes that the next-hop router is closer to the destination
  Steps:
    Search routing table for complete matched IP address
      Send to next-hop router or to the directly connected NIC
    Search routing table for matched network ID
      Send to next-hop router or to the directly connected NIC
    Search routing table for default route
      Send to this default next-hop router
    host or network unreachable

## Slide 31: Network Layer – IP Routing (3)
Ex1: routing in the same network
  bsdi: 140.252.13.35
  sun: 140.252.13.33
Ex Routing table:
140.252.13.33 00:d0:59:83:d9:16 UHLW fxp1
bsdi
sun
link hdr
IP hdr
destination network = 140.252.13.0
.13.35
.13.33
Ethernet, 140.252.13
dest IP = 140.252.13.33
dest Enet = Enet of 140.252.13.33

## Slide 32: Network Layer – IP Routing (4)
Ex2:
  routing across multi-network
gateway
netb
link hdr
IP hdr
next hop = 140.252.104.2 (default)
.1.4
.1.183
Ethernet, 140.252.1
dest IP = 192.48.96.9
dest Enet = Enet of 140.252.1.4
bsdi
sun
link hdr
IP hdr
next hop = 140.252.13.33 (default)
.13.35
.13.33
Ethernet, 140.252.13
dest IP = 192.48.96.9
dest Enet = Enet of 140.252.13.33
next hop = 140.252.1.183 (default)
modem
modem
IP hdr
dest IP = 192.48.96.9
SLIP
next hop = 140.252.1.4 (default)
.1.29

## Slide 33: ARP and RARP
Something between MAC (link layer) And IP (network layer)

## Slide 34: ARP and RARP
ARP – Address Resolution Protocol and RARP – Reverse ARP
  Mapping between IP and Ethernet address
When an Ethernet frame is sent on LAN from one host to another,
  It is the 48-bit Ethernet address that determines for which interface the frame is destined
32-bit Internet address
48-bit Ethernet address
RARP
ARP

## Slide 35: ARP and RARP – ARP Example
Example
  % ftp bsd1
  (4) next-hop or direct host
  (5) Search ARP cache
  (6) Broadcast ARP request
  (7) bsd1 response ARP reply
  (9) Send original IP datagram
FTP
TCP
IP
Ethernet
Driver
resolver
hostname
IP addr
hostname
ARP
Ethernet
Driver
Ethernet
Driver
ARP
ARP
IP
TCP
ARP request (Ethernet broadcast)
establish connection with IP address
send IP datagram to IP address
(1)
(2)
(3)
(4)
(5)
(6)
(7)
(8)
(9)

## Slide 36: ARP and RARP – ARP Cache
Maintain recent ARP results
  Come from both ARP request and reply
  Expiration time
    Complete entry = 20 minutes
    Incomplete entry = 3 minutes
  Use arp command to see the cache
  E.g.:
    $ arp -a
    $ arp -da
    $ arp -S 140.113.235.132 00:0e:a6:94:24:6e
$ arp -a
crypto23.csie.nctu.edu.tw (140.113.208.143) at 00:16:e6:5b:fa:e9 on fxp1 [ethernet]
e3rtn-208.csie.nctu.edu.tw (140.113.208.254) at 00:0e:38:a4:c2:00 on fxp1 [ethernet]
e3rtn-210.csie.nctu.edu.tw (140.113.210.254) at 00:0e:38:a4:c2:00 on fxp2 [ethernet]

## Slide 37: ARP and RARP – ARP/RARP Packet Format
Ethernet destination addr: all 1’s (broadcast)
Known value for IP <-> Ethernet
  Frame type: 0x0806 for ARP, 0x8035 for RARP
  Hardware type: type of hardware address (1 for Ethernet)
  Protocol type: type of upper layer address (0x0800 for IP)
  Hard size: size in bytes of hardware address (6 for Ethernet)
  Protocol size: size in bytes of upper layer address (4 for IP)
  Op: 1, 2, 3, 4 for ARP request, reply, RARP request, reply
op
sender Ethernet addr
sender IP addr
target Ethernet addr
target IP addr
prot type
hard type
frame type
Ethernet source addr
Ethernet destination addr
6
6
2
2
2
1
1
2
6
4
6
4
hard size
prot size
Ethernet header
28 byte ARP request/reply

## Slide 38: ARP and RARP – Use tcpdump to see ARP
Host 140.113.17.212 => 140.113.17.215
  Clear ARP cache of 140.113.17.212
    $ sudo arp -d 140.113.17.215
  Run tcpdump on 140.113.17.215 (00:11:d8:06:1e:81)
    $ sudo tcpdump -i sk0 -e arp
    $ sudo tcpdump -i sk0 -n -e arp
    $ sudo tcpdump -i sk0 -n -t -e arp
  On 140.113.17.212, ssh to 140.113.17.215
15:18:54.899779 00:90:96:23:8f:7d > Broadcast, ethertype ARP (0x0806), length 60:
arp who-has nabsd tell chbsd.csie.nctu.edu.tw
15:18:54.899792 00:11:d8:06:1e:81 > 00:90:96:23:8f:7d, ethertype ARP (0x0806), length 42:
arp reply nabsd is-at 00:11:d8:06:1e:81
15:26:13.847417 00:90:96:23:8f:7d > ff:ff:ff:ff:ff:ff, ethertype ARP (0x0806), length 60:
arp who-has 140.113.17.215 tell 140.113.17.212
15:26:13.847434 00:11:d8:06:1e:81 > 00:90:96:23:8f:7d, ethertype ARP (0x0806), length 42:
arp reply 140.113.17.215 is-at 00:11:d8:06:1e:81
00:90:96:23:8f:7d > ff:ff:ff:ff:ff:ff, ethertype ARP (0x0806), length 60:
arp who-has 140.113.17.215 tell 140.113.17.212
00:11:d8:06:1e:81 > 00:90:96:23:8f:7d, ethertype ARP (0x0806), length 42:
arp reply 140.113.17.215 is-at 00:11:d8:06:1e:81

## Slide 39: ARP and RARP – Proxy ARP
Let router answer ARP request on one of its networks for a host on another of its network
bsdi
sun
.35
.33
Ethernet, 140.252.13
svr4
.34
slip
SLIP
.65
.66
modem
modem
netb
Ethernet, subnet 140.252.1
gemini
ARP request for 140.252.1.29
ARP reply
140.252.1.183
Telebit NetBlazer router configured to act as proxy ARP agent for sun
140.252.1.29
SLIP (dualup)

## Slide 40: ARP and RARP – Gratuitous ARP
Gratuitous ARP
  The host sends an ARP request looking for its own IP
  Provide two features
    Used to determine whether there is another host configured with the same IP
    Used to cause any other host to update ARP cache when changing hardware address

## Slide 41: ARP and RARP – RARP
Principle
  Used for the diskless system to read its hardware address from the NIC and send an RARP request to gain its IP
RARP Server Design
  RARP server must maintain the map from hardware address to an IP address for many host
  Link-layer broadcast
    This prevent most routers from forwarding an RARP request

## Slide 42: ICMP
Internet Control Message Protocol

## Slide 43: ICMP – Introduction
Part of the IP layer
  ICMP messages are transmitted within IP datagram
  ICMP communicates error messages and other conditions that require attention for other protocols
ICMP message format
IP header
ICMP message
20 bytes
IP datagram
8-bit type
8-bit code
16-bit checksum
(content depends on type and code)
0
7 8
15 16
31

## Slide 44: ICMP – Message Type (1)
type | code | Description | Query | Error
0 | 0 | echo reply (Ping reply) | ● | 
3 |  | destination unreachable: |  | 
 | 0 | > network unreachable |  | ●
 | 1 | > host unreachable |  | ●
 | 2 | > protocol unreachable |  | ●
 | 3 | > port unreachable |  | ●
 | 4 | > fragmentation needed but don’t fragment bit set |  | ●
 | 5 | > source route failed |  | ●
 | 6 | > destination network unknown |  | ●
 | 7 | > destination host unknown |  | ●
 | 8 | > source host isolated (obsolete) |  | ●
 | 9 | > destination network administratively prohibited |  | ●
 | 10 | > destination host administratively prohibited |  | ●
type | code | Description | Query | Error
 | 11 | > network unreachable for TOS |  | ●
 | 12 | > host unreachable for TOS |  | ●
 | 13 | > communication administratively prohibited by filtering |  | ●
 | 14 | > host precedence violation |  | ●
 | 15 | > precedence cutoff effect |  | ●

## Slide 45: ICMP – Message Type (2)
type | code | Description | Query | Error
4 | 0 | source quench (elementary flow control) |  | ●
5 |  | redirect: |  | 
 | 0 | > redirect for network |  | ●
 | 1 | > redirect for host |  | ●
 | 2 | > redirect for type-of-service and network |  | ●
 | 3 | > redirect for type-of-service and host |  | ●
8 | 0 | echo request (Ping request) | ● | 
9 | 0 | router advertisement | ● | 
10 | 0 | router solicitation | ● | 
11 |  | time exceeded: |  | 
 | 0 | > time-to-live equals 0 during transit (Traceroute) |  | ●
 | 1 | > time-to-live equals 0 during reassembly |  | ●
type | code | Description | Query | Error
12 |  | parameter problem: |  | 
 | 0 | > IP header bad (catchall error) |  | ●
 | 1 | > required option missing |  | ●
13 | 0 | timestamp request | ● | 
14 | 0 | timestamp reply | ● | 
15 | 0 | information request (obsolete) | ● | 
16 | 0 | information reply (obsolete) | ● | 
17 | 0 | address mask request | ● | 
18 | 0 | address mask reply |  | 

## Slide 46: ICMP – Query Message – Address Mask Request/Reply (1)
Address Mask Request and Reply
  Used for diskless system to obtain its subnet mask
  Identifier and sequence number
    Can be set to anything for sender to match reply with request
  The receiver will response an ICMP reply with the subnet mask of the receiving NIC
type (17 or 18)
code (0)
checksum
address mask
0
7 8
15 16
31
identifier
sequence number

## Slide 47: ICMP – Query Message – Address Mask Request/Reply (2)
Example:
$ ping -M m sun1.cs.nctu.edu.tw
ICMP_MASKREQ
PING sun1.cs.nctu.edu.tw (140.113.235.171): 56 data bytes
68 bytes from 140.113.235.171: icmp_seq=0 ttl=251 time=0.663 ms mask=255.255.255.0
68 bytes from 140.113.235.171: icmp_seq=1 ttl=251 time=1.018 ms mask=255.255.255.0
68 bytes from 140.113.235.171: icmp_seq=2 ttl=251 time=1.028 ms mask=255.255.255.0
68 bytes from 140.113.235.171: icmp_seq=3 ttl=251 time=1.026 ms mask=255.255.255.0
^C
--- sun1.cs.nctu.edu.tw ping statistics ---
4 packets transmitted, 4 packets received, 0% packet loss
round-trip min/avg/max/stddev = 0.663/0.934/1.028/0.156 ms
$ icmpquery -m sun1
sun1 : 0xFFFFFF00
※ icmpquery can be found in /usr/ports/net-mgmt/icmpquery

## Slide 48: ICMP – Query Message – Timestamp Request/Reply (1)
Timestamp request and reply
  Allow a system to query another for the current time
  Milliseconds resolution, since midnight UTC
  Requestor
    Fill in the originate timestamp and send
  Reply system
    Fill in the receive timestamp when it receives the request and the transmit time when it sends the reply
type (13 or 14)
code (0)
checksum
originate timestamp
0
7 8
15 16
31
identifier
sequence number
receive timestamp
transmit timestamp

## Slide 49: ICMP – Query Message – Timestamp Request/Reply (2)
Example
$ ping -M time nabsd
ICMP_TSTAMP
PING nabsd.cs.nctu.edu.tw (140.113.17.215): 56 data bytes
76 bytes from 140.113.17.215: icmp_seq=0 ttl=64 time=0.663 ms
tso=06:47:46 tsr=06:48:24 tst=06:48:24
76 bytes from 140.113.17.215: icmp_seq=1 ttl=64 time=1.016 ms
tso=06:47:47 tsr=06:48:25 tst=06:48:25
$ icmpquery -t nabsd
nabsd : 14:54:47
$ sudo tcpdump -i sk0 -e icmp
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on sk0, link-type EN10MB (Ethernet), capture size 96 bytes
14:48:24.999106 00:90:96:23:8f:7d > 00:11:d8:06:1e:81, ethertype IPv4 (0x0800), length 110:
chbsd.csie.nctu.edu.tw > nabsd: ICMP time stamp query id 18514 seq 0, length 76
14:48:24.999148 00:11:d8:06:1e:81 > 00:90:96:23:8f:7d, ethertype IPv4 (0x0800), length 110:
nabsd > chbsd.csie.nctu.edu.tw: ICMP time stamp reply id 18514 seq 0: org 06:47:46.326,
recv 06:48:24.998, xmit 06:48:24.998, length 76
14:48:26.000598 00:90:96:23:8f:7d > 00:11:d8:06:1e:81, ethertype IPv4 (0x0800), length 110:
chbsd.csie.nctu.edu.tw > nabsd: ICMP time stamp query id 18514 seq 1, length 76
14:48:26.000618 00:11:d8:06:1e:81 > 00:90:96:23:8f:7d, ethertype IPv4 (0x0800), length 110:
nabsd > chbsd.csie.nctu.edu.tw: ICMP time stamp reply id 18514 seq 1: org 06:47:47.327,
recv 06:48:25.999, xmit 06:48:25.999, length 76

## Slide 50: ICMP – Error Message – Destination Unreachable Error Message
Format
  8 bytes ICMP Header
  Application-depend data portion
    IP header
      Let ICMP know how to interpret the 8 bytes that follow
    first 8 bytes that followed this IP header
      Information about who generates the error
type (3)
code (0-15)
checksum
IP header (including options) + first 8 bytes of original IP datagram data
0
7 8
15 16
31
Unused (must be 0)
8 bytes

## Slide 51: ICMP – Error Message – Port Unreachable (1)
ICMP port unreachable
  Type = 3 , code = 3
  Host receives a UDP datagram but the destination port does not correspond to a port that some process has in use
Ethernet header
IP header
ICMP header
IP header of datagram that generated error
UDP header
14 bytes
20 bytes
8 bytes
20 bytes
8 bytes
ICMP message
IP datagram
data portion of ICMP message

## Slide 52: ICMP – Error Message – Port Unreachable (2)
Example:
  Using TFTP (Trivial File Transfer Protocol)
    Original port: 69
$ tftp
tftp> connect localhost 8888
tftp> get temp.foo
Transfer timed out.
tftp>
$ sudo tcpdump -i lo0
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on lo0, link-type NULL (BSD loopback), capture size 96 bytes
15:01:24.788511 IP localhost.62089 > localhost.8888: UDP, length 16
15:01:24.788554 IP localhost > localhost:
ICMP localhost udp port 8888 unreachable, length 36
15:01:29.788626 IP localhost.62089 > localhost.8888: UDP, length 16
15:01:29.788691 IP localhost > localhost:
ICMP localhost udp port 8888 unreachable, length 36

## Slide 53: ICMP – Ping Program (1)
Use ICMP to test whether another host is reachable
  Type 8, ICMP echo request
  Type 0, ICMP echo reply
ICMP echo request/reply format
  Identifier: process ID of the sending process
  Sequence number: start with 0
  Optional data: any optional data sent must be echoed
type (0 or 8)
code (0)
checksum
optional data
0
7 8
15 16
31
identifier
sequence number
8 bytes

## Slide 54: ICMP – Ping Program (2)
Ex:
  ServerA ping ServerB
  execute “tcpdump -i sk0 -X -e icmp” on ServerB
ServerA $ ping ServerB
PING ServerB.cs.nctu.edu.tw (140.113.17.215): 56 data bytes
64 bytes from 140.113.17.215: icmp_seq=0 ttl=64 time=0.520 ms
15:08:12.631925 00:90:96:23:8f:7d > 00:11:d8:06:1e:81, ethertype IPv4 (0x0800), length 98:
ServerA.cs.nctu.edu.tw > ServerB: ICMP echo request, id 56914, seq 0, length 64
0x0000: 4500 0054 f688 0000 4001 4793 8c71 11d4 E..T....@.G..q..
0x0010: 8c71 11d7 0800 a715 de52 0000 45f7 9f35 .q.......R..E..5
0x0020: 000d a25a 0809 0a0b 0c0d 0e0f 1011 1213 ...Z............
0x0030: 1415 1617 1819 1a1b 1c1d 1e1f 2021 2223 .............!"#
0x0040: 2425 2627 2829 2a2b 2c2d 2e2f 3031 3233 $%&'()*+,-./0123
0x0050: 3435 45
15:08:12.631968 00:11:d8:06:1e:81 > 00:90:96:23:8f:7d, ethertype IPv4 (0x0800), length 98:
ServerB > ServerA.cs.nctu.edu.tw: ICMP echo reply, id 56914, seq 0, length 64
0x0000: 4500 0054 d97d 0000 4001 649e 8c71 11d7 E..T.}..@.d..q..
0x0010: 8c71 11d4 0000 af15 de52 0000 45f7 9f35 .q.......R..E..5
0x0020: 000d a25a 0809 0a0b 0c0d 0e0f 1011 1213 ...Z............
0x0030: 1415 1617 1819 1a1b 1c1d 1e1f 2021 2223 .............!"#
0x0040: 2425 2627 2829 2a2b 2c2d 2e2f 3031 3233 $%&'()*+,-./0123
0x0050: 3435 45
Type/Code
ID

## Slide 55: ICMP – Ping Program (3)
To get the route that packets take to host
  Taking use of “IP Record Route Option”
  Command: ping -R
  Cause every router that handles the datagram to add its (outgoing) IP address to a list in the options field.
  Format of Option field for IP RR Option
    code: type of IP Option (7 for RR)
    len: total number of bytes of the RR option
    ptr:4 ~ 40 used to point to the next IP address
  Only 9 IP addresses can be stored
    Limitation of IP header
4-bit version
4-bit header length
8-bit type of service (TOS)
16-bit total length (in bytes)
16-bit identification
3-bit flags
13-bit fragment offset
32-bit source IP address
32-bit destination IP address
options (if any)
data
8-bit time to live (TTL)
8-bit protocol
16-bit header checksum
0
15 16
31
20 bytes
IP header
ICMP message
20 bytes
IP datagram
code
len
ptr
IP addr #1
IP addr #2
IP addr #3
...
IP addr #9
1
1
1
4 bytes
4 bytes
4 bytes
4 bytes
ptr = 4
ptr = 8
ptr = 12
ptr = 36
ptr = 40
39 bytes

## Slide 56: ICMP – Ping Program (4)
Example:
bsdi
sun
.35
.33
Ethernet
svr4
.34
slip
SLIP
.65
.66
empty list
3rd = 140.252.13.35
1st = 140.252.13.66
2nd= 140.252.13.65
4th = 140.252.13.34
srv4 $ ping -R slip
PING slip (140.252.13.65): 56 data bytrs
64 bytes from 140.252.13.65: icmp_seq=0 ttl=254 time=280 ms
RR bsdi (140.252.13.66)
bsdi (140.252.13.65)
bsdi (140.252.13.35)
bsdi (140.252.13.34)
64 bytes from 140.252.13.65: icmp_seq=1 ttl=254 time=280 ms (same route)
64 bytes from 140.252.13.65: icmp_seq=2 ttl=254 time=270 ms (same route)
^?
--- slip ping statistics
3 packets transmitted, 3 packets received, 0% packet loss
round-trip min/avg/max = 270/276/280 ms

## Slide 57: ICMP – Ping Program (5)
Example:
$ ping -R www.nctu.edu.tw
PING www.nctu.edu.tw (140.113.250.5): 56 data bytes
64 bytes from 140.113.250.5: icmp_seq=0 ttl=61 time=2.361 ms
RR: ProjE27-253.NCTU.edu.tw (140.113.27.253)
140.113.0.57
CC250-gw.NCTU.edu.tw (140.113.250.253)
www.NCTU.edu.tw (140.113.250.5)
www.NCTU.edu.tw (140.113.250.5)
140.113.0.58
ProjE27-254.NCTU.edu.tw (140.113.27.254)
e3rtn.csie.nctu.edu.tw (140.113.17.254)
chbsd.csie.nctu.edu.tw (140.113.17.212)
64 bytes from 140.113.250.5: icmp_seq=1 ttl=61 time=3.018 ms (same route)
$ sudo tcpdump -v -n -i dc0 -e icmp
tcpdump: listening on dc0, link-type EN10MB (Ethernet), capture size 96 bytes
22:57:04.507271 00:90:96:23:8f:7d > 00:90:69:64:ec:00, ethertype IPv4 (0x0800), length 138:
(tos 0x0, ttl 64, id 17878, offset 0, flags [none], proto: ICMP (1), length: 124,
options ( RR (7) len 390.0.0.00.0.0.00.0.0.00.0.0.00.0.0.00.0.0.00.0.0.00.0.0.00.0.0.0EOL
(0) len 1 )) 140.113.17.212 > 140.113.250.5: ICMP echo request, id 45561, seq 0, length 64
22:57:04.509521 00:90:69:64:ec:00 > 00:90:96:23:8f:7d, ethertype IPv4 (0x0800), length 138:
(tos 0x0, ttl 61, id 33700, offset 0, flags [none], proto: ICMP (1), length: 124,
options ( RR (7) len 39140.113.27.253, 140.113.0.57, 140.113.250.253, 140.113.250.5,
140.113.250.5, 140.113.0.58, 140.113.27.254, 140.113.17.254, 0.0.0.0EOL (0) len 1 ))
140.113.250.5 > 140.113.17.212: ICMP echo reply, id 45561, seq 0, length 64

## Slide 58: Traceroute Program (1)
To print the route packets take to network host
Drawbacks of IP RR options (ping -R)
  Not all routers have supported the IP RR option
  Limitation of IP header length
Background knowledge of traceroute
  When a router receive a datagram, it will decrement the TTL by one
  When a router receive a datagram with TTL = 0 or 1,
    it will through away the datagram and
    sends back a “Time exceeded” ICMP message
  Unused UDP port will generate a “port unreachable” ICMP message

## Slide 59: Traceroute Program (2)
Operation of traceroute
  Send UDP with port > 30000, encapsulated with IP header with TTL = 1, 2, 3, … continuously
  When router receives the datagram and TTL = 1, it returns a “Time exceeded” ICMP message
  When destination host receives the datagram and TTL = 1, it returns a “Port unreachable” ICMP message
source host
router
router
destination host
IP (TTL=1)
ICMP (time exceeded)
source host
router
router
destination host
IP (TTL=2)
ICMP (time exceeded)
IP (TTL=1)
ICMP (time exceeded)
source host
router
router
destination host
IP (TTL=3)
ICMP (port unreachable)
IP (TTL=2)
ICMP (port unreachable)
IP (TTL=1)
ICMP (port unreachable)

## Slide 60: Traceroute Program (3)
Time exceed ICMP message
  Type = 11, code = 0 or 1
    Code = 0 means TTL=0 during transit
    Code = 1 means TTL=0 during reassembly
  First 8 bytes of datagram
    UDP header
TYPE (11)
CODE (0 or 1)
CHECKSUM
UNUSED (MUST BE ZERO)
INTERNET HEADER + FIRST 64 BITS OF DATAGRAM
...
0
8
16
31

## Slide 61: Traceroute Program (4)
Example
$ traceroute bsd1.cs.nctu.edu.tw
traceroute to bsd1.cs.nctu.edu.tw (140.113.235.131), 64 hops max, 40 byte packets
1 e3rtn.csie.nctu.edu.tw (140.113.17.254) 0.377 ms 0.365 ms 0.293 ms
2 ProjE27-254.NCTU.edu.tw (140.113.27.254) 0.390 ms 0.284 ms 0.391 ms
3 140.113.0.58 (140.113.0.58) 0.292 ms 0.282 ms 0.293 ms
4 140.113.0.165 (140.113.0.165) 0.492 ms 0.385 ms 0.294 ms
5 bsd1.cs.nctu.edu.tw (140.113.235.131) 0.393 ms 0.281 ms 0.393 ms
$ sudo tcpdump -i sk0 -t icmp
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on sk0, link-type EN10MB (Ethernet), capture size 96 bytes
IP e3rtn.csie.nctu.edu.tw > nabsd: ICMP time exceeded in-transit, length 36
IP e3rtn.csie.nctu.edu.tw > nabsd: ICMP time exceeded in-transit, length 36
IP e3rtn.csie.nctu.edu.tw > nabsd: ICMP time exceeded in-transit, length 36
IP ProjE27-254.NCTU.edu.tw > nabsd: ICMP time exceeded in-transit, length 36
IP ProjE27-254.NCTU.edu.tw > nabsd: ICMP time exceeded in-transit, length 36
IP ProjE27-254.NCTU.edu.tw > nabsd: ICMP time exceeded in-transit, length 36
IP 140.113.0.58 > nabsd: ICMP time exceeded in-transit, length 36
IP 140.113.0.58 > nabsd: ICMP time exceeded in-transit, length 36
IP 140.113.0.58 > nabsd: ICMP time exceeded in-transit, length 36
IP 140.113.0.165 > nabsd: ICMP time exceeded in-transit, length 36
IP 140.113.0.165 > nabsd: ICMP time exceeded in-transit, length 36
IP 140.113.0.165 > nabsd: ICMP time exceeded in-transit, length 36
IP bsd1.cs.nctu.edu.tw > nabsd: ICMP bsd1.cs.nctu.edu.tw udp port 33447 unreachable, length 36
IP bsd1.cs.nctu.edu.tw > nabsd: ICMP bsd1.cs.nctu.edu.tw udp port 33448 unreachable, length 36
IP bsd1.cs.nctu.edu.tw > nabsd: ICMP bsd1.cs.nctu.edu.tw udp port 33449 unreachable, length 36

## Slide 62: Traceroute Program (5)
The router IP in traceroute is the interface that receives the datagram. (incoming IP)
  Traceroute from left host to right host
    if1, if3
  Traceroute from right host to left host
    if4, if2
router 1
router 2
network 2
if2
if3
if1
if4
network 1
network 3

## Slide 63: Traceroute Program – IP Source Routing Option (1)
Source Routing
  Sender specifies the route
Two forms of source routing
  Strict source routing
    Sender specifies the exact path that the IP datagram must follow
  Loose source routing
    As strict source routing, but the datagram can pass through other routers between any two addresses in the list
Format of IP header option field
  Code = 0x89 for strict and code = 0x83 for loose SR option
code
len
ptr
IP addr #1
IP addr #2
IP addr #3
...
IP addr #9
1
1
1
4 bytes
4 bytes
4 bytes
4 bytes
ptr = 4
ptr = 8
ptr = 12
ptr = 36
ptr = 40
39 bytes
4-bit version
4-bit header length
8-bit type of service (TOS)
16-bit total length (in bytes)
16-bit identification
3-bit flags
13-bit fragment offset
32-bit source IP address
32-bit destination IP address
options (if any)
data
8-bit time to live (TTL)
8-bit protocol
16-bit header checksum
0
15 16
31
20 bytes

## Slide 64: Traceroute Program – IP Source Routing Option (2)
Scenario of source routing
  Sending host
    Remove first entry and append destination address in the final entry of the list
  Receiving router != destination
    Loose source route, forward it as normal
  Receiving router = destination
    Next address in the list becomes the destination
    Change source address
    Increment the pointer
S
R1
R2
R3
D
dest = D { #R1, R2, R3}
dest = R1 { #R2, R3, D}
dest = R2 { R1, #R3, D}
dest = R3 { R1, R2, #D}
dest = D { R1, R2, R3#}

## Slide 65: Traceroute Program – IP Source Routing Option (3)
Traceroute using IP loose SR option
Example:
$ traceroute u2.nctu.edu.tw
traceroute to u2.nctu.edu.tw (211.76.240.193), 64 hops max, 40 byte packets
1 e3rtn-235 (140.113.235.254) 0.549 ms 0.434 ms 0.337 ms
2 140.113.0.166 (140.113.0.166) 108.726 ms 4.469 ms 0.362 ms
3 v255-194.NTCU.net (211.76.255.194) 0.529 ms 3.446 ms 5.464 ms
4 v255-229.NTCU.net (211.76.255.229) 1.406 ms 2.017 ms 0.560 ms
5 h240-193.NTCU.net (211.76.240.193) 0.520 ms 0.456 ms 0.315 ms
$ traceroute -g 140.113.0.149 u2.nctu.edu.tw
traceroute to u2.nctu.edu.tw (211.76.240.193), 64 hops max, 48 byte packets
1 e3rtn-235 (140.113.235.254) 0.543 ms 0.392 ms 0.365 ms
2 140.113.0.166 (140.113.0.166) 0.562 ms 9.506 ms 0.624 ms
3 140.113.0.149 (140.113.0.149) 7.002 ms 1.047 ms 1.107 ms
4 140.113.0.150 (140.113.0.150) 1.497 ms 6.653 ms 1.595 ms
5 v255-194.NTCU.net (211.76.255.194) 1.639 ms 7.214 ms 1.586 ms
6 v255-229.NTCU.net (211.76.255.229) 1.831 ms 9.244 ms 1.877 ms
7 h240-193.NTCU.net (211.76.240.193) 1.440 ms !S 2.249 ms !S 1.737 ms !S

## Slide 66: IP Routing – Processing in IP Layer
IP layer
IP output: calculate next hop router (if necessary)
our packet (one of our IP addresses or broadcast addrs) ?
process IP options
IP input queue
ICMP
routing table
UDP
TCP
routing daemon
route command
netstat command
network interface
yes
no
source routing
forward datagram (if forwarding enable)
ICMP redirects
routing table updates from adjacent routers

## Slide 67: IP Routing – Routing Table (1)
Routing Table
  Command to list: netstat -rn
  Flag
    U: the route is up
    G: the route is to a router (indirect route)
      Indirect route: IP is the dest. IP, MAC is the router’s MAC
    H: the route is to a host (Not to a network)
      The dest. filed is either an IP address or network address
    S: the route is static
  Expire: expiration time for each route
$ netstat -rn
Routing tables
Internet:
Destination Gateway Flags Netif Expire
Default 140.113.17.254 UGS em0
127.0.0.1 link#2 UH lo0
140.113.17.0/24 link#1 U em0
140.113.17.225 link#1 UHS lo0

## Slide 68: IP Routing – Routing Table (2)
Example:
srv4 $ netstat -rn
Routing tables
Destination Gateway Flags Refcnt Use Interface
140.252.13.65 140.252.13.35 UGH 0 0 emd0
127.0.0.1 127.0.0.1 UH 1 0 lo0
default 140.252.13.33 UG 0 0 emd0
140.252.13.32 140.252.13.34 U 4 25043 emd0
dst. = sun
dst. = slip
dst. = 192.207.117.2
dst. = svr4 or 140.252.13.34
dst. = 127.0.0.1
bsdi
sun
.35
.33
Ethernet, subnet 140.252.13.32
svr4
.34
slip
SLIP
.65
.66
subnet 140.252.13.64
gateway
Internet
.4
140.252.104.1
Ethernet, subnet 140.252.1
140.252.1.29
loopback

## Slide 69: ICMP – No Route to Destination
If there is no match in routing table
  If the IP datagram is generated on the host
    “host unreachable” or “network unreachable”
  If the IP datagram is being forwarded
    ICMP “host unreachable” error message is generated and sends back to sending host
    ICMP message
      Type = 3, code = 0 for host unreachable
      Type = 3, code = 1 for network unreachable
type (3)
code (0-15)
checksum
IP header (including options) + first 8 bytes of original IP datagram data
0
7 8
15 16
31
Unused (must be 0)
8 bytes

## Slide 70: ICMP – Redirect Error Message (1)
Concept
  Used by router to inform the sender that the datagram should be sent to a different router
  This will happen if the host has a choice of routers to send the packet to
    Ex:
      R1 found sending and receiving interface are the same
host
R2
R1
final destination
(1) IP datagram
(2) IP datagram
(3) ICMP redirect

## Slide 71: ICMP – Redirect Error Message (2)
ICMP redirect message format
  Code 0: redirect for network
  Code 1: redirect for host
  Code 2: redirect for TOS and network (RFC 1349)
  Code 3: redirect for TOS and hosts (RFC 1349)
type (3)
code (0-15)
checksum
IP header (including options) + first 8 bytes of original IP datagram data
0
7 8
15 16
31
Route IP address that should be used
8 bytes

## Slide 72: ICMP – Router Discovery Messages (1)
Dynamic update host’s routing table
  ICMP router solicitation message (懇求)
    Host broadcast or multicast after bootstrapping
  ICMP router advertisement message
    Router response
    Router periodically broadcast or multicast
Format of ICMP router solicitation message
type (0)
code (0)
checksum
0
7 8
15 16
31
Unused (sent as 0)
8 bytes

## Slide 73: ICMP – Router Discovery Messages (2)
Format of ICMP router advertisement message
  Router address
    Must be one of the router’s IP address
  Preference level
    Preference as a default router address
type (0)
code (0)
checksum
0
7 8
15 16
31
preference level [1]
8 bytes
number of addresses
address entry size (2)
lifetime
router address [1]
router address [2]
preference level [2]
...

## Slide 74: UDP – User Datagram Protocol

## Slide 75: UDP
No reliability
  Datagram-oriented, not stream-oriented protocol
UDP header
  8 bytes
  Source port and destination port
    Identify sending and receiving process
  UDP length: ≧ 8
16-bit destination port number
data (if any)
0
7 8
15 16
31
16-bit UDP length
16-bit UDP checksum
8 bytes
16-bit source port number

## Slide 76: UDP
Application
  VoIP
  VPN (OpenVPN over UDP)
  DNS
  SNMP
  Quick UDP Internet Connections (QUIC)
    Designed by Google, based on UDP
    Renamed to “HTTP/3”
    Keep reliability as TCP, but less latency
      As most HTTP connections will demand TLS, QUIC makes the exchange of setup keys and supported protocols part of the initial handshake process.
      During network-switch events, reuse old connection instead of creating a new one as TCP does.

## Slide 77: TCP – Transmission Control Protocol

## Slide 78: TCP
Services
  Connection-oriented
    Establish TCP connection before exchanging data
  Reliability
    Acknowledgement when receiving data
    Retransmission when timeout
    Ordering
    Discard duplicated data
    Flow control

## Slide 79: TCP – Header (1)
16-bit destination port number
32-bit sequence number
options (if any)
data (if any)
32-bit acknowledgment number
0
15 16
31
20 bytes
16-bit window size
16-bit urgent pointer
16-bit TCP checksum
4-bit header length
reserved (6 bits)
U R G
ACK
PSH
RST
SYN
FIN
16-bit source port number

## Slide 80: TCP – Header (2)
Flags
  SYN
    Establish new connection
  ACK
    Acknowledgement number is valid
    Used to ack previous data that host has received
  RST
    Reset connection
  FIN
    The sender is finished sending data

## Slide 81: TCP connection – establishment and termination
segment 1
segment 2
segment 3
segment 4
segment 5
segment 6
segment 7
SYN 1415531521:1415531521(0) <mss 1024>
SYN 1823083521:1823083521(0) ACK 1415531522, <mss 1024>
ACK 1823083522
FIN 1415531522:1415531522(0) ACK 1823083522
ACK 1415531523
FIN 1823083522:1823083522(0) ACK 1415531523
ACK 1823083523
Three-way handshake
TCP’s half close

## Slide 82: Appendix

## Slide 83: Introduction – Encapsulation
Multiplexing
  Gathering data from multiple sockets, enveloping data with header
user data
user data
Appl header
application data
TCP header
application data
TCP header
IP header
application data
TCP header
IP header
Ethernet header
Ethernet trailer
TCP segment
IP datagram
Ethernet frame
Ethernet driver
application
TCP
IP
Ethernet

## Slide 84: Introduction – Decapsulation
Demultiplexing
  Delivering received segments to correct socket
demultiplexing based on destination port number in TCP or UDP header
ICMP
IGMP
TCP
UDP
Ethernet
Driver
ARP
RARP
IP
Incoming frame
demultiplexing based on frame type in Ethernet header
Application
Application
...
Application
Application
...
demultiplexing based on protocol value in IP header

## Slide 85: Introduction – Addressing
Addressing
  Nearby (same network)
FTP
Client
FTP
Server
TCP
TCP
IP
IP
Ethernet
Driver
Ethernet
Driver
FTP Protocol
TCP Protocol
IP Protocol
Ethernet Protocol
Ethernet
Application
Transport
Network
Link
User
Process
Kernel
Handles
Application
Details
Handles
Communication
Details

## Slide 86: Introduction – Addressing
Addressing
  Faraway (across network)
FTP
Client
FTP
Server
TCP
TCP
IP
IP
Ethernet
Driver
Ethernet
Driver
FTP Protocol
TCP Protocol
IP Protocol
Ethernet
Protocol
Application
Transport
Network
Link
IP
Ethernet
Driver
Token ring
Driver
Token ring
Protocol
Ethernet
IP Protocol
Router
Token Ring

## Slide 87: Network Layer – IP Header (1)
Version (4-bit)
  4 for IPv4 and 6 for IPv6
Header length (4-bit)
  The number of 32-bit words in the header (15*4=60 bytes)
  Normally, the value is 5 (no option)
TOS - Type of Service (8-bit)
  IP Precedence: 3-bit precedence + 4-bit TOS + 1-bit unused
  DSCP: 3-bit major class + 3-bit drop preference + 2-bit ECN
Total length (16-bit)
  Total length of the IP datagram in bytes
DSCP: Differentiated Services Code Point
ECN: Explicit Congestion Notification
Name | Binary Value
Routine | 000
Priority | 001
Unneduate | 010
Flash | 011
Flash Override | 100
Critic/critical | 010
Internetwork Control | 110
Network Control | 111
Application | Minimize delay | Maximize throughput | Maximize reliability | Minimize monetary cost | Hex value
Telnet/Rlogin | 1 | 0 | 0 | 0 | 0x10
FTP control | 1 | 0 | 0 | 0 | 0x10
FTP data | 0 | 1 | 0 | 0 | 0x08
any bulk data | 0 | 1 | 0 | 0 | 0x08
TFTP | 1 | 0 | 0 | 0 | 0x10
SMTP command phase | 1 | 0 | 0 | 0 | 0x10
4-bit version
4-bit header length
8-bit type of service (TOS)
16-bit total length (in bytes)
16-bit identification
3-bit flags
13-bit fragment offset
32-bit source IP address
32-bit destination IP address
options (if any)
data
8-bit time to live (TTL)
8-bit protocol
16-bit header checksum
0
15 16
31
20 bytes

## Slide 88: Network Layer – IP Header (2)
DSCP - Differentiated Services Code Point (6-bit)
  Supersede the ToS field in IPv4 to make
  per-hop behavior (PHB) decisions
    Default
      Best-effort traffic
    Expedited Forwarding (EF)
      Dedicated to low-loss, low-latency traffic
    Class Selector
      Backward compatibility with the IP Precedence field
    Assured Forwarding (AF)
      Give assurance of delivery under prescribed conditions
ECN: Explicit Congestion Notification (2-bit)
  FreeBSD 8.0 implement ECN support for TCP
    Enable ECN via sysctl(8)
      net.inet.tcp.ecn.enable=1
    Linux Kernel supports ECN for TCP since version 2.4.20
DSCP Class Selector Names | Binary DSCP Values | IPP Binary Values | IPP Names
Default/CS0* | 000000 | 000 | Routine
CS1 | 001000 | 001 | Priority
CS2 | 010000 | 010 | Immediate
CS3 | 011000 | 011 | Flash
CS4 | 100000 | 100 | Flash Override
CS5 | 101000 | 101 | Critic/Critical
CS6 | 110000 | 110 | Internetwork Control
CS7 | 111000 | 111 | Network Control
Queue Class | Low Drop Probability | Medium Drop Probability | High Drop Probability
 | Name/Dec/Bin | Name/Dec/Bin | Name/Dec/Bin
1 | AF11 / 10 / 001010 | AF12 / 12 / 001100 | AF13 / 14 / 001110
2 | AF21 / 18 / 010010 | AF22 / 20 / 010100 | AF23 / 22 / 010110
4 | AF31 / 26 / 011010 | AF32 / 28 / 011100 | AF33 / 30 / 011110
5 | AF41 / 34 /100010 | AF42 / 36 / 100100 | AF43 /38 / 100110
Binary Value | Description
00 | Non ECN-Capable Transport, Non-ECT
10 | ECN Capable Transport, ECT(0)
01 | ECN Capable Transport, ECT(1)
11 | Congestion Encountered, CE
4-bit version
4-bit header length
8-bit type of service (TOS)
16-bit total length (in bytes)
16-bit identification
3-bit flags
13-bit fragment offset
32-bit source IP address
32-bit destination IP address
options (if any)
data
8-bit time to live (TTL)
8-bit protocol
16-bit header checksum
0
15 16
31
20 bytes

## Slide 89: Network Layer – IP Header (3)
Identification (16-bit)
  Identify the group of fragments of a single IP datagram
Fragmentation offset (13-bit)
  Specify the offset of a particular fragment relative to the beginning of the original unfragmented IP datagram
Flags (3-bit)
  All these three fields are used for fragmentation
4-bit version
4-bit header length
8-bit type of service (TOS)
16-bit total length (in bytes)
16-bit identification
3-bit flags
13-bit fragment offset
32-bit source IP address
32-bit destination IP address
options (if any)
data
8-bit time to live (TTL)
8-bit protocol
16-bit header checksum
0
15 16
31
20 bytes
Reserved | Don’t Fragment (DF) | More Fragments (MF)

## Slide 90: Network Layer – IP Header (4)
TTL (8-bit)
  Limit of next hop count of routers
Protocol (8-bit)
  Used to demultiplex to other protocols
  TCP, UDP, ICMP, IGMP
Header checksum (16-bit)
  Calculated over the IP header only
  If checksum error, IP discards the datagram and no error message is generated
4-bit version
4-bit header length
8-bit type of service (TOS)
16-bit total length (in bytes)
16-bit identification
3-bit flags
13-bit fragment offset
32-bit source IP address
32-bit destination IP address
options (if any)
data
8-bit time to live (TTL)
8-bit protocol
16-bit header checksum
0
15 16
31
20 bytes

## Slide 91: IP Fragmentation (1)
MTU limitation
  Before network-layer to link-layer
    IP will check the size and link-layer MTU
    Do fragmentation if necessary
  Fragmentation may be done at sending host or routers
  Reassembly is done only in receiving host
IP header
UDP header
UDP data
IP datagram (1501 bttes)
20 bytes
8 bytes
1473 bytes
IP header
UDP header
UDP data
20 bytes
8 bytes
1473 bytes
packet (1500 bytes)
IP header
20 bytes
1 byte
packet

## Slide 92: IP Fragmentation (1)
IP header
UDP header
UDP data
IP datagram (1501 bttes)
20 bytes
8 bytes
1473 bytes
IP header
UDP header
UDP data
20 bytes
8 bytes
1473 bytes
packet (1500 bytes)
IP header
20 bytes
1 byte
packet
identification: which unique IP datagram
flags: more fragments?
fragment offset offset of this datagram from the beginning of original datagram
identification: the same
flags: more fragments
fragment offset 0
identification: the same
flags: end of fragments
fragment offset 1480

## Slide 93: IP Fragmentation (3)
Issues of fragmentation
  One fragment lost, entire datagram must be retransmitted
  If the fragmentation is performed by intermediate router, there is no way for sending host how fragmentation did
  Fragmentation is often avoided
    There is a “don’t fragment” bit in flags of IP header
4-bit version
4-bit header length
8-bit type of service (TOS)
16-bit total length (in bytes)
16-bit identification
3-bit flags
13-bit fragment offset
32-bit source IP address
32-bit destination IP address
options (if any)
data
8-bit time to live (TTL)
8-bit protocol
16-bit header checksum
0
15 16
31
20 bytes

## Slide 94: ICMP Unreachable Error – Fragmentation Required
Type=3, code=4
  Router will generate this error message if the datagram needs to be fragmented, but the “don’t fragment” bit is turn on in IP header
Message format
type (3)
code (4)
checksum
IP header (including options) + first 8 bytes of original IP datagram data
0
7 8
15 16
31
8 bytes
Unused (must be 0)
MTU of next-hop network

## Slide 95: ICMP – Source Quench Error
Type=4, code=0
  May be generated by system when it receives datagram at a rate that is too fast to be processed
  Host receiving more than it can handle datagram
    Send ICMP source quench or
    Throw it away
  Host receiving UDP source quench message
    Ignore it or
    Notify application

## Slide 96: Appendix of IP Options: IP Timestamp Option
IP Timestamp Option
  Similar to RR option
  Record Timestamp in option field
    code, len, ptr are the same as IP RR option
    OF
      Overflow field
      Router will increment OF if it can’t add a timestamp because of no room left
    FL
      Flags
      0: only timestamp
      1: both timestamp and IP address
      3: the sender initiates the options with up to 4 pairs of IP address and timestamp
code
len
ptr
timestamp #1
timestamp #2
timestamp #3
...
timestamp #9
1
1
1
4 bytes
4 bytes
4 bytes
4 bytes
40 bytes
OF
FL