## Slide 1: VPN Virtual Private Network

## Slide 2: Introduction
Uses public telecommunication channels, such as the Internet or other network service, instead of leased lines channels.
Described as Virtual because it is distant connection using private connections.
Used to widely now because of today's globalization.
Connects users or branches.
Used to use dial-up or Leased communication, now using IP-VPN’s

## Slide 3: What is VPN
Extension of a private network that encompasses links across shared or public networks like the Internet.
Enable to send data between two computers across a shared or public internetwork in a manner that emulates the properties of a point-to-point private link.
VPN Server
Web Server
Firewall
Internet
VPN Client
Tunnel
VPN Connection
Private Network

## Slide 4: Common Uses of VPNs (1/3)
1. Remote Access Over the Internet
Virtual Private Networking: An Overview | Microsoft Docs

## Slide 5: Common Uses of VPNs (2/3)
2. Connecting Networks Over the Internet (Site to Site VPN)
Virtual Private Networking: An Overview | Microsoft Docs

## Slide 6: Common Uses of VPNs (3/3)
3. Connecting Computers over an Intranet (similar to 1.)
Virtual Private Networking: An Overview | Microsoft Docs

## Slide 7: Why Use VPN?
Cheap
  Legacy private network uses remote connectivity through dial-up modems or through leased line connections, it’s expensive.
Scalable
  Extending a leased line connection is complex.
  Easy to administer.
Security
  Provide encryption and file integrity.

## Slide 8: VPN Key Concept - Tunneling
VPN consists of a set of point to point connections tunneled over the Internet.
In order to achieve tunneling, the packets are encapsulated as the payload of packets.
  Payloads, to and from addresses, port numbers and other standard protocol packet headers
  As seen by the external routers carrying the connection
Host
Transit Internet work
Tunnel
Tunnel Endpoint
Host
Transit Internetwork Header
Tunneled Payload
Payload
Payload

## Slide 9: Basic VPN Requirements
User Authentication
Key Management
Address Management
Data Encryption

## Slide 10: Basic VPN Requirements (1/2)
User Authentication
  Verify the VPN client's identity and restrict VPN access to authorized users only.
  Provide audit and accounting records to show who accessed what information and when.
  X.509, pre-shared key, etc.
Key Management
  Generate and refresh encryption keys for the client and the server.
  Simple Key Management for IP: ISAKMP/Oakley, etc.

## Slide 11: Basic VPN Requirements (2/2)
Address Management
  Assign a VPN client's address on the intranet and ensure that private addresses are kept private
Data Encryption
  No one outside the VPN can alter the VPN.
  Data carried on the public network must be rendered unreadable to unauthorized clients on the network.

## Slide 12: VPN Security
Authentication
  Ensuring that the data originates at the source that it claims.
Access Control
  Restricting unauthorized users from gaining admission to the network.
Confidentiality
  Preventing anyone from reading or copying data as it travels across the Internet.
Data Integrity
  Ensuring that no one tampers with data as it travels across the Internet.

## Slide 13: Common Implementations
Based on PPP
  Point-to-Point Tunneling Protocol (PPTP) (PPP + encryption + GRE)
  Layer Two Tunneling Protocol (L2TP) (PPTP + L2F)
Based on TCP/IP
  L2TP/IPsec
  IPsec Tunnel mode [RFC 4301]
  BGP/MPLS IP VPN [RFC 4364]
SSL/TLS
  Secure Socket Tunneling Protocol (SSTP) (PPTP + SSL)
  SSL VPN
  OpenVPN

## Slide 14: PPP - Point-to-Point Protocol
PPP [RFC 1661] provides a standard method for transporting multi-protocol datagrams over point-to-point (direct) links.
  Data link layer (layer 2) protocol
Three components
  Encapsulation (for transporting purpose)
  Link Control Protocol (for data-link connectability)
  Network Control Protocols (NCP) family (L3 management support)
Extra Options
  Authentication: PAP, CHAP, EAP, MS-CHAP, MS-CHAPv2, etc.
  Link Quality and error detection
  Compression
  Encryption: MPPC + MPPE, etc.
  Multilink (MP, The PPP Multilink Protocol)

## Slide 15: Tunneling Protocol
Allows a network user to access or provide a network service that the underlying network does not support or provide directly. (Wikipedia)
GRE (Generic Routing Encapsulation): Establish a virtual point-to-point connection between two networks.
  IP as a delivery protocol
  Virtual Tunnel: (Tunnel) IP header + GRE packet header
  Encapsulation, not encryption
PPTP / L2TP
IPsec
OpenVPN (with SSL/TLS)
etc.

## Slide 16: PPTP - Point-to-Point Tunneling Protocol
PPTP [RFC 2637] uses an enhanced GRE mechanism to provide a flow- and congestion-controlled (TCP) encapsulated datagram service for carrying PPP packets.
PPTP creates a GRE tunnel through which the PPTP GRE packets are sent.
PPP header
PPP payload (IP datagram, IPX datagram, MetBEUI frame)
PPP frame
Encrypted
GRE header
IP header

## Slide 17: Security of PPTP
PPTP has been the subject of many security analyses and
serious security vulnerabilities have been found
  MS-CHAP is fundamentally insecure.
  MS-CHAPv2 is vulnerable to dictionary attack on the captured challenge response packets.
The PPP payload can be encrypted by using Microsoft Point to Point Encryption (MPPE) when using MS-CHAPv1/v2
EAP-TLS (Extensible Authentication Protocol – TLS) is the superior authentication choice for PPTP.

## Slide 18: L2TP - Layer Two Tunneling Protocol
L2TP [RFC 2661]: PPTP + L2F (Layer Two Forwarding)
High level protocols (e.g., PPP) establish L2TP session (“call”) within the L2TP tunnel, and traffic for each session is isolated.
A tunnel can contains multiple connections at once.
L2TP over IP internetworks uses UDP and a series of L2TP messages for tunnel maintenance.
L2TPv3 provides additional security features, improved encapsulation, and the ability to carry data links other than simply PPP over an IP network. (Wikipedia)
PPP frame
PPP header
PPP payload (IP datagram, IPX datagram, MetBEUI frame)
L2TP header
UDP header
IP header
L2TP frame
UDP message

## Slide 19: L2TP/IPsec
L2TP does not provide confidentiality or strong authentication.
Usually use IPsec ESP (Encapsulating Security Payload) to encrypt the L2TP packet.
  Data encryption begins before the PPP connection process by negotiating an IPSec security association.
  Require computer-level authentication using computer certificates.
PPP header
PPP payload (IP datagram, IPX datagram, MetBEUI frame)
L2TP header
UDP header
IP header
PPP header
PPP payload (IP datagram, IPX datagram, MetBEUI frame)
L2TP header
UDP header
IPSec ESP header
IP header
IPSec
ESP
trailer
IPSec
Auth
trailer
Encrypted by IPSec

## Slide 20: IPsec
IPsec [RFC 4301] is a secure network protocol suite provides authentication and encryption ability over IPv4 network.
Two modes in IPsec
  Transport mode: Insert IPsec header (AH/ESP) between IP and TCP header, then modify original IP header.
  Tunnel mode: Encapsulate original packet, and prepend new IP and IPsec header.
Two functions that ensure confidentiality:
  Authentication Header (AH)
    Provide source authentication and integrity without encryption.
  Encapsulating Security Payload (ESP)
    Provide both data authentication, data integrity and data encryption.
Security Associations (SA) provides the parameters necessary for AH and/or ESP operations.
  IKE (Internet Key Exchange): Provide authentication and key exchange. e.g., ISAKMP, OAKLEY

## Slide 21: IPsec Modes
IPsec VPN Theory | Cisco Routing & Switching and Security (jazier.blogspot.com)

## Slide 22: SSL VPN
A form of VPN that can be used with a standard Web browser.
  Also can be used to tunnel traffic via SSL or TLS protocol
The traffic is encrypted with the SSL protocol or Transport Layer Security (TLS) protocol.
Proprietary software
  Cisco AnyConnect
  Juniper Networks Pulse Secure
  Fortigate
Open Source
  OpenVPN

## Slide 23: Appendix
I Am Anonymous When I Use a VPN – 10 Myths Debunked
Virtual Private Networking: An Overview
BeyondCorp by Google: Protected connection from untrusted networks without the use of a VPN.
  See also: Role-Based Access Control (RBAC)
Protocol reference
  VPN
  PPP / GRE / PPTP / L2TP
  IPsec / IKE
  IP protocol numbers