## Slide 1: Advanced Topics of Mail Service Deal with Malicious Mails in the Real World
lwhsu (2020-2023, CC-BY)
? (?-2019)

## Slide 2: Nature of Spam
Spam – Simultaneously Posted Advertising Message
  UBE – Unsolicited Bulk Email
  UCE – Unsolicited Commercial Email
Spam
  There is no relationship between receiver and
    Sender
    Message content
  Opt-out instruction
  Conceal trail
    False return address
    Forged header information
  Use misconfigured mail system to be an accomplice
  Circumvent spam filters either encode message or insert random letters
https://en.wikipedia.org/wiki/Spam_(food)#/media/File:Spam_2.jpg

## Slide 3: Problems of Spam
Cost
  Waste bandwidth and disk space
  DoS like side-effect
  Waste time
  False deletion
  Bounce messages of nonexistent users
    Nonexistent return address
    Forged victim return address
Detection
  Aggressive spam policy may cause high false positive

## Slide 4: SPAM detection
SPAM vs. non-SPAM
  Mail sent by spammer vs. non-spammer
Problem of SPAM mail
  About 90% of E-mail are SPAM! Useless for mankind!
SPAM detection
  Client-based detection
    spammer detection
    cost-effective, which can easily reach over 95% accuracy
  Content-based detection
    spam detection
    costly with less than 90% accuracy, needing training and computation
  Who is the winner? Client-based? Content-based? (or Spammer?)
  Endless war between the administrators and spammers.

## Slide 5: Anti–SPAM – Client – Based Detection
Client-blocking
  Check their IP address, hostnames, email address, and/or behavior when the client connect to send a message
  Problems
    IP address, hostname, email address are forged
    Innocent victim open relay host
Techniques
  DNSBL/WL (DNS Blacklists and Whitelists)
    RFC 5782
  Greylisting
  SPF – Sender Policy Framework
  DomainKeys/DKIM
  Sender ID
  …

## Slide 6: Anti–SPAM – Content – Based Detection
Spam patterns in message header/body
  Encrypted
  Encoded
Techniques
  Pattern detection
  Bayesian spam filtering
  …
Difficulties
  Embed HTML codes within words of their message to break up phrases
  Randomly inserted words
  Slower and resource consumption

## Slide 7: Anti–SPAM – Action
When you suspect that a mail is spam, you can:
  Reject
    immediately during the SMTP conversation
    directly discard the mail without notifying someone else
  Save spam into a suspected spam repository
  Label spam and deliver it with some kind of spam tag
  Ex:
    X-Spam-Status: Yes, hits=18.694 tagged_above=3 required=6.3
    X-Spam-Level: ******************
    X-Spam-Flag: YES

## Slide 8: Client – based Detections
Fight with spammers:
  DNSBL/WL
    DNS-based blacklist/whitelist for suspected/trusted senders(IP address)
  Greylisting
    client-based method that can stop mail coming from some spamming programs
  SPF (Sender Policy Framework)
    A client-based method to detect whether a client is authorized or not
    Sender ID
      NOT the new SPF
      http://www.open-spf.org/SPF_vs_Sender_ID/

## Slide 9: DNSxL
What DNSBL/WL maintainers do
  Suppose cs.nctu.edu.tw has a DNSxL database
    DNSBL Domain “dnsbl.cs.nctu.edu.tw”
  If 140.112.23.118 is detected as open relay
    Add resource record 118.23.112.140.dnsbl.cs.nctu.edu.tw
  When we receive a connection from 140.112.23.118
    DNS query for 118.23.112.140.dnsbl.cs.nctu.edu.tw
      A 127.0.0.2 (SHOULD in 127.0.0.0/8)
        https://www.spamhaus.org/zen/
        TXT Reason
  Right-Hand Sde Blacklist (RHSBL)
Using DNSBL
  Review their service options and policies carefully
  https://www.dnsbl.info/dnsbl-database-check.php

## Slide 10: Greylisting (1/2)
https://greylisting.org
Client-based (receiver) method that can stop (slowdown) some spammers
Different behaviors against SMTP response codes
  While spammers prefer to send mail to other recipients rather than keeping log and retrying later, MTAs have the responsibility of retrying a deferred mail (in 10-30 mins)
    Combine with other spam mitigations and network security features
Response Codes | 2xx | 4xx | 5xx
Normal MTA | Success | Retry later | Give-up
Most Spammers | Success | Ignore and send another | Give-up

## Slide 11: Greylisting (2/2)
Idea of greylisting:
  Taking use of 4xx SMTP response code to stop steps of spamming programs
Steps:
  Pair (recipient, client-ip)
  Reply a 4xx code for the first coming of every (recipient, client-ip) pair.
  Allow retrial of this mail after a period of time (usually 5~20 mins)
    Suitable waiting time will make the spamming programs giving up this mail
Limitation
  Can NOT detect “open relay” mail servers

## Slide 12: Sender Policy Framework (SPF)
A client-based method to detect whether a client is authorized or not
http://www.open-spf.org/
  RFC 4408

## Slide 13: Sender Policy Framework (SPF) – Is following mail questionable?
Delivered-To: lwhsu.gmail@gmail.com
Received: by 10.204.137.3 with SMTP id u3cs64867bkt;
Sat, 21 May 2011 13:19:49 -0700 (PDT)
Received: by 10.68.58.38 with SMTP id n6mr1407584pbq.5.1306009188186;
Sat, 21 May 2011 13:19:48 -0700 (PDT)
Return-Path: <lwhsu@cs.nctu.edu.tw>
Received: from zfs.cs.nctu.edu.tw (zfs.cs.nctu.edu.tw [140.113.17.215])
by mx.google.com with ESMTP id a2si4001228pbs.91.2011.05.21.13.19.46;
Sat, 21 May 2011 13:19:46 -0700 (PDT)
Received: from zfs.cs.nctu.edu.tw (localhost [127.0.0.1])
by zfs.cs.nctu.edu.tw (Postfix) with ESMTP id 50E2A4ABC5
for <lwhsu.gmail@gmail.com>; Sun, 22 May 2011 04:16:08 +0800 (CST)
Date: Sun, 22 May 2011 04:12:57 +0800
From: Li-Wen Hsu <lwhsu@cs.nctu.edu.tw>
To: Li-Wen Hsu <lwhsu.gmail@gmail.com>
Subject: test
Message-ID: <20110521201257.GA58179@zfs.cs.nctu.edu.tw>
this is a test
Notes: Is zfs authorized?

## Slide 14: Sender Policy Framework (SPF) – SMTP trace
zfs-$ telnet zfs.cs.nctu.edu.tw 25
220 zfs.cs.nctu.edu.tw ESMTP Postfix
helo zfs.cs.nctu.edu.tw
250 zfs.cs.nctu.edu.tw
mail from: <lwhsu@cs.nctu.edu.tw>
250 2.1.0 Ok
rcpt to: <lwhsu.gmail@gmail.com>
250 2.1.5 Ok
data
354 End data with <CR><LF>.<CR><LF>
Date: Sun, 22 May 2011 04:12:57 +0800
From: Li-Wen Hsu <lwhsu@cs.nctu.edu.tw>
To: Li-Wen Hsu <lwhsu.gmail@gamil.com>
Subject: test
Message-ID: <20110521201257.GA58179@zfs.cs.nctu.edu.tw>
this is a test
.
250 2.0.0 Ok: queued as 50E2A4ABC5

## Slide 15: Sender Policy Framework (SPF) – With SPF detection
Delivered-To: lwhsu.gmail@gmail.com
Received: by 10.204.137.3 with SMTP id u3cs64867bkt;
Sat, 21 May 2011 13:19:49 -0700 (PDT)
Received: by 10.68.58.38 with SMTP id n6mr1407584pbq.5.1306009188186;
Sat, 21 May 2011 13:19:48 -0700 (PDT)
Return-Path: <lwhsu@cs.nctu.edu.tw>
Received: from zfs.cs.nctu.edu.tw (zfs.cs.nctu.edu.tw [140.113.17.215])
by mx.google.com with ESMTP id a2si4001228pbs.91.2011.05.21.13.19.46;
Sat, 21 May 2011 13:19:46 -0700 (PDT)
Received-SPF: softfail (google.com: domain of transitioning lwhsu@cs.nctu.edu.tw does not designate 140.113.17.215 as permitted sender) client-ip=140.113.17.215;
Authentication-Results: mx.google.com; spf=softfail (google.com: domain of transitioning lwhsu@cs.nctu.edu.tw does not designate 140.113.17.215 as permitted sender) smtp.mail=lwhsu@cs.nctu.edu.tw
Received: from zfs.cs.nctu.edu.tw (localhost [127.0.0.1])
by zfs.cs.nctu.edu.tw (Postfix) with ESMTP id 50E2A4ABC5
for <lwhsu.gmail@gmail.com>; Sun, 22 May 2011 04:16:08 +0800 (CST)
Date: Sun, 22 May 2011 04:12:57 +0800
From: Li-Wen Hsu <lwhsu@cs.nctu.edu.tw>
To: Li-Wen Hsu <lwhsu.gmail@gmail.com>

## Slide 16: Sender Policy Framework (SPF) – The idea
For a domain administrator, they can claim which mail servers will be used in his environment
  Ex. For cs.nctu.edu.tw, {csmailer,csmailgate,csmail}.cs.nctu.edu.tw are the authorized mail servers
    Mail out from these servers are authorized mail (under control of administrator)
    Other mail might be forged and have higher probability to be SPAMs
SPF technique specifies all possible outgoing mail clients in the TXT/SPF record of DNS service to claim the authorized mail servers
When destination MTA receives a mail, it will check the client IP:
  For a mail out from authorized servers, it should be safe.
  For a mail out from unauthorized servers, it might be forged.

## Slide 17: SPF Record Syntax – Mechanisms (1/2)
TXT/SPF record: v=spf1 [qualifier][mechanism]
all
  Always matches
  Usually at the end of the SPF record
ip4 (NOT ipv4)
  ip4: <ip4-address>
  ip4: <ip4-network>/<prefix-length>
ip6 (NOT ipv6)
  ip6:<ip6-address>
  ip6:<ip6-network>/<prefix-length>
a
  a
  a/<prefix-length>
  a:<domain>
  a:<domain>/<prefix-length>
The content of this page and following are from http://www.open-spf.org/SPF_Record_Syntax

## Slide 18: SPF Record Syntax – Mechanisms (2/2)
mx
  mx
  mx/<prefix-length>
  mx:<domain>
  mx:<domain>/<prefix-length>
ptr
  ptr
  ptr:<domain>
exists
  exists:<domain>
    Does A record exist?
include
  include:<domain>
    Warning: If the domain does not have a valid SPF record, the result is a permanent error. Some mail receivers will reject based on a PermError

## Slide 19: SPF Record Syntax - Qualifiers & Evaluation
Qualifiers
  + Pass (default qualifier)
  - Fail
  ~ SoftFail
  ? Neutral
Evaluation
  Mechanisms are evaluated in order: (first-matching)
    If a mechanism results in a hit, its qualifier value is used
    If no mechanism or modifier matches, the default result is "Neutral"
  Ex.
    "v=spf1 +a +mx -all"
    "v=spf1 a mx -all"

## Slide 20
Result | Explanation | Intended action
Pass | The SPF record designates the host to be allowed to send | Accept
Fail | The SPF record has designated the host as NOT being allowed to send | Reject
SoftFail | The SPF record has designated the host as NOT being allowed to send but is in transition | Accept but mark
Neutral | The SPF record specifies explicitly that nothing can be said about validity | Accept
None | The domain does not have an SPF record or the SPF record does not evaluate to a result | Accept
PermError | A permanent error has occurred (eg. Badly formatted SPF record) | Unspecified
TempError | A transient error has occurred | Accept or reject
SPF Record Syntax - Evaluation Results

## Slide 21: SPF Record Syntax – Modifier
redirect
  redirect=<domain>
  The SPF record for domain replace the current record. The macro-expanded domain is also substituted for the current-domain in those look-ups
exp
  exp=<domain>
  If an SMTP receiver rejects a message, it can include an explanation. An SPF publisher can specify the explanation string that senders see. This way, an ISP can direct nonconforming users to a web page that provides further instructions about how to configure SASL
  The domain is expanded; a TXT lookup is performed. The result of the TXT query is then macro-expanded and shown to the sender. Other macros can be used to provide an customized explanation

## Slide 22: Sender Policy Framework (SPF) – Example of mail from an authorized server
On bsd2.cs.nctu.edu.tw
  From: lwhsu@cs.nctu.edu.tw
  To: lwhsu.gmail@gmail.com
Related SPF Record:
cs.nctu.edu.tw
"v=spf1 a mx a:csmailer.cs.nctu.edu.tw a:csmailgate.cs.nctu.edu.tw a:csmail.cs.nctu.edu.tw ~all"

## Slide 23: Sender Policy Framework (SPF) – Example of mail from an authorized server
Delivered-To: lwhsu.gmail@gmail.com
Received: by 10.90.56.12 with SMTP id e12cs464421aga;
Sun, 10 May 2009 12:12:00 -0700 (PDT)
Received: by 10.210.91.17 with SMTP id o17mr7881766ebb.3.1241982719273;
Sun, 10 May 2009 12:11:59 -0700 (PDT)
Return-Path: <lwhsu@cs.nctu.edu.tw>
Received: from csmailer.cs.nctu.edu.tw (csmailer.cs.nctu.edu.tw [140.113.235.130])
by mx.google.com with ESMTP id 10si4213172eyz.41.2009.05.10.12.11.58;
Sun, 10 May 2009 12:11:59 -0700 (PDT)
Received-SPF: pass (google.com: domain of lwhsu@cs.nctu.edu.tw
designates 140.113.235.130 as permitted sender) client-ip=140.113.235.130;
Authentication-Results: mx.google.com; spf=pass (google.com: domain of lwhsu@cs.nctu.edu.tw designates 140.113.235.130 as permitted sender) smtp.mail=lwhsu@cs.nctu.edu.tw
Received: from bsd2.cs.nctu.edu.tw (bsd2 [140.113.235.132])
by csmailer.cs.nctu.edu.tw (Postfix) with ESMTP id 189DA3F65E
for <lwhsu.gmail@gmail.com>; Mon, 11 May 2009 03:11:57 +0800 (CST)
Received: (from lwhsu@localhost)
by bsd2.cs.nctu.edu.tw (8.14.3/8.14.2/Submit) id n4AJBuTM000652
for lwhsu.gmail@gmail.com; Mon, 11 May 2009 03:11:56 +0800 (CST)
(envelope-from lwhsu)
Date: Mon, 11 May 2009 03:11:56 +0800
From: Li-Wen Hsu <lwhsu@cs.nctu.edu.tw>
To: lwhsu.gmail@gmail.com
Subject: test if SPF record works

## Slide 24: Sender Policy Framework (SPF) – Example of Forged Headers
On zfs.cs.nctu.edu.tw
Envelope From: lwhsu@zfs.cs.nctu.edu.tw
Mail Headers
  From: lwhsu@cs.nctu.edu.tw
  To: lwhsu.gmail@gmail.com
Related SPF Records:
cs.nctu.edu.tw | zfs.cs.nctu.edu.tw
"v=spf1 a mx a:csmailer.cs.nctu.edu.tw a:csmailgate.cs.nctu.edu.tw a:csmail.cs.nctu.edu.tw ~all" | "v=spf1 a ~all"

## Slide 25: Sender Policy Framework (SPF) – Example of Forged Headers
Delivered-To: lwhsu.gmail@gmail.com
Received: by 10.223.112.14 with SMTP id u14cs45092fap;
Mon, 23 May 2011 03:08:04 -0700 (PDT)
Received: by 10.236.80.65 with SMTP id j41mr2678377yhe.192.1306145283043;
Mon, 23 May 2011 03:08:03 -0700 (PDT)
Return-Path: <lwhsu@zfs.cs.nctu.edu.tw>
Received: from zfs.cs.nctu.edu.tw (zfs.cs.nctu.edu.tw [140.113.17.215])
by mx.google.com with ESMTP id 57si13494424yhl.14.2011.05.23.03.08.01;
Mon, 23 May 2011 03:08:02 -0700 (PDT)
Received-SPF: pass (google.com: domain of lwhsu@zfs.cs.nctu.edu.tw designates
140.113.17.215 as permitted sender) client-ip=140.113.17.215;
Authentication-Results: mx.google.com; spf=pass (google.com: domain of
lwhsu@zfs.cs.nctu.edu.tw designates 140.113.17.215 as permitted sender)
smtp.mail=lwhsu@zfs.cs.nctu.edu.tw
Received: by zfs.cs.nctu.edu.tw (Postfix, from userid 1001)
id EBCF04B638; Mon, 23 May 2011 18:04:23 +0800 (CST)
Date: Mon, 23 May 2011 18:04:23 +0800
From: Li-Wen Hsu <lwhsu@cs.nctu.edu.tw>
To: lwhsu.gmail@gmail.com
Subject: test SPF
This is a SPF test.

## Slide 26: Sender Policy Framework (SPF) – SPF and Forwarding
Does SPF break forwarding?
  Yes, but only if the receiver checks SPF without understanding their mail receiving architecture
  Workaround
    http://www.open-spf.org/FAQ/Forwarding
SRS: Sender Rewriting Scheme
  Forwarders should apply Sender Rewriting Scheme (SRS) to rewrite the sender address after SPF checks
    http://www.open-spf.org/SRS

## Slide 27: Sender Policy Framework (SPF) – Forwarding Example (no sender rewrite)
On gmail (lwhsu.gmail’s account)
  Envelope From: lwhsu.gmail@gmail.com
Mail Headers
  From: lwhsu@cs.nctu.edu.tw
  To: lwhsu@lwhsu.org
On knight.lwhsu.org (lwhsu.org’s mx)
  ~lwhsu/.forward:
    liwenhsu.gmail@gmail.com
gmail.com | _spf.google.com
"v=spf1 redirect=_spf.google.com" | "v=spf1 ip4:216.239.32.0/19 ip4:64.233.160.0/19 ip4:66.249.80.0/20 ip4:72.14.192.0/18 ip4:209.85.128.0/17 ip4:66.102.0.0/20 ip4:74.125.0.0/16 ip4:64.18.0.0/20 ip4:207.126.144.0/20 ip4:173.194.0.0/16 ?all"

## Slide 28
Delivered-To: liwenhsu.gmail@gmail.com
Received: by 10.229.81.4 with SMTP id v4cs221969qck;
Sun, 10 May 2009 11:09:26 -0700 (PDT)
Received: by 10.216.2.84 with SMTP id 62mr2907141wee.217.1241978964147;
Sun, 10 May 2009 11:09:24 -0700 (PDT)
Return-Path: <lwhsu.gmail@gmail.com>
Received: from knight.lwhsu.ckefgisc.org (lwhsusvr.cs.nctu.edu.tw [140.113.24.67])
by mx.google.com with ESMTP id 24si6143118eyx.13.2009.05.10.11.09.22;
Sun, 10 May 2009 11:09:23 -0700 (PDT)
Received-SPF: neutral (google.com: 140.113.24.67 is neither permitted nor denied by domain
of lwhsu.gmail@gmail.com) client-ip=140.113.24.67;
Authentication-Results: mx.google.com; spf=neutral (google.com: 140.113.24.67 is neither
permitted nor denied by domain of lwhsu.gmail@gmail.com)
smtp.mail=lwhsu.gmail@gmail.com;
Received: by knight.lwhsu.ckefgisc.org (Postfix)
id 47F571143E; Mon, 11 May 2009 02:09:21 +0800 (CST)
Delivered-To: lwhsu@lwhsu.org
Received: from an-out-0708.google.com (an-out-0708.google.com [209.85.132.243])
by knight.lwhsu.ckefgisc.org (Postfix) with ESMTP id D832B11431
for <lwhsu@lwhsu.org>; Mon, 11 May 2009 02:09:20 +0800 (CST)
Received: by an-out-0708.google.com with SMTP id d14so1324869and.41
for <lwhsu@lwhsu.org>; Sun, 10 May 2009 11:09:19 -0700 (PDT)
Sender: lwhsu.gmail@gmail.com
Received: by 10.100.248.4 with SMTP id v4mr14373811anh.121.1241978954295; Sun,
10 May 2009 11:09:14 -0700 (PDT)
Date: Mon, 11 May 2009 02:09:13 +0800
Message-ID: <ef417ae30905101109j5c7b27bcy70a5bcf6d58092ab@mail.gmail.com>
Subject: test SPF
From: Li-Wen Hsu <lwhsu@cs.nctu.edu.tw>
To: lwhsu@lwhsu.org

## Slide 29: Sender Policy Framework (SPF) – Some More Examples
Outgoing Mail Gateway
  List all authorized senders of cs.nctu.edu.tw
Incoming Mail Gateway
  BIND releases from 9.4.0 support the SPF RR type
cs.nctu.edu.tw. 3600 IN TXT "v=spf1 a mx a:farewell.cs.nctu.edu.tw a:csmailer.cs.nctu.edu.tw a:tcsmailer.cs.nctu.edu.tw a:tcsmailer2.cs.nctu.edu.tw ~all"
csmx1.cs.nctu.edu.tw. 3600 IN TXT "v=spf1 a -all"
csmx2.cs.nctu.edu.tw. 3600 IN TXT "v=spf1 a -all"
csmx3.cs.nctu.edu.tw. 3600 IN TXT "v=spf1 a -all"
When a mail server sends a bounce message (returned mail), it uses a null MAIL FROM: <>, and a HELO address that's supposed to be its own name. SPF will still operate, but in "degraded mode" by using the HELO domain name instead.

## Slide 30: Sender Policy Framework (SPF) – Backward Compatibility (1/2)
Delivered-To: lwhsu.gmail@gmail.com
Received: by 10.90.56.12 with SMTP id e12cs719147aga;
Tue, 12 May 2009 00:49:39 -0700 (PDT)
Received: by 10.224.2.85 with SMTP id 21mr5508548qai.262.1242114578996;
Tue, 12 May 2009 00:49:38 -0700 (PDT)
Return-Path: <lwhsu@freebsd.cs.nctu.edu.tw>
Received: from FreeBSD.cs.nctu.edu.tw (FreeBSD.cs.nctu.edu.tw [140.113.17.209])
by mx.google.com with ESMTP id 7si4128629qwf.35.2009.05.12.00.49.38;
Tue, 12 May 2009 00:49:38 -0700 (PDT)
Received-SPF: pass (google.com: best guess record for domain of
lwhsu@freebsd.cs.nctu.edu.tw designates 140.113.17.209 as permitted sender)
client-ip=140.113.17.209;
Authentication-Results: mx.google.com; spf=pass (google.com: best guess record for
domain of lwhsu@freebsd.cs.nctu.edu.tw designates 140.113.17.209 as permitted
sender) smtp.mail=lwhsu@freebsd.cs.nctu.edu.tw
Received: by FreeBSD.cs.nctu.edu.tw (Postfix, from userid 1058)
id 6D98E61DBC; Tue, 12 May 2009 15:49:37 +0800 (CST)
Date: Tue, 12 May 2009 15:49:37 +0800
From: Li-Wen Hsu <lwhsu@FreeBSD.org>
To: lwhsu.gmail@gmail.com
Subject: test tw.freebsd.org SPF
When there is no SPF record, guess by A record

## Slide 31: Sender Policy Framework (SPF) – Backward Compatibility (2/2)
Delivered-To: lwhsu.gmail@gmail.com
Received: by 10.90.56.12 with SMTP id e12cs719801aga;
Tue, 12 May 2009 00:56:27 -0700 (PDT)
Received: by 10.224.74.84 with SMTP id t20mr5499756qaj.328.1242114987266;
Tue, 12 May 2009 00:56:27 -0700 (PDT)
Return-Path: <lwhsu@freebsd.cs.nctu.edu.tw>
Received: from FreeBSD.cs.nctu.edu.tw (FreeBSD.cs.nctu.edu.tw [140.113.17.209])
by mx.google.com with ESMTP id 5si4111810qwh.54.2009.05.12.00.56.26;
Tue, 12 May 2009 00:56:27 -0700 (PDT)
Received-SPF: pass (google.com: domain of lwhsu@freebsd.cs.nctu.edu.tw
designates 140.113.17.209 as permitted sender) client-ip=140.113.17.209;
Authentication-Results: mx.google.com; spf=pass (google.com: domain of
lwhsu@freebsd.cs.nctu.edu.tw designates 140.113.17.209 as permitted sender)
smtp.mail=lwhsu@freebsd.cs.nctu.edu.tw
Received: by FreeBSD.cs.nctu.edu.tw (Postfix, from userid 1058)
id 78CD461DB0; Tue, 12 May 2009 15:56:25 +0800 (CST)
Date: Tue, 12 May 2009 15:56:25 +0800
From: Li-Wen Hsu <lwhsu@FreeBSD.org>
To: lwhsu.gmail@gmail.com
Subject: test tw.freebsd.org SPF (2)
Comparative result – when SPF record available:

## Slide 32: Sender Policy Framework (SPF) – Example of include mechanism
nctucs [~] -wangth- dig pixnet.net txt
;; ANSWER SECTION:
pixnet.net. 86400 IN TXT "v=spf1 include:aspmx.googlemail.com include:amazonses.com ip4:60.199.247.0/24 ip4:103.23.108.0/24 ip4:103.23.109.0/24 ip4:113.196.243.0/26 ~all"
Notes: 搭配 google app 使用

## Slide 33: DomainKeys and DKIM
Verify the source of a mail
  Allows an organization to claim responsibility for transmitting a message, in a way that can be validated by a recipient
  With few computation cost
Consortium spec
  Derived from Yahoo DomainKeys and Cisco Identified Internet Mail
  RFCs
    RFC 4870 Domain-Based Email Authentication Using Public Keys Advertised in the DNS (DomainKeys)
    RFC 4871 DomainKeys Identified Mail (DKIM) Signatures
  https://www.dkim.org/
    https://www.dkim.org/info/DKIM-teaser.ppt

## Slide 34: DKIM: Goals
Validate message content, itself
  Not related to path
Transparent to end users
  No client User Agent upgrades are required
  But extensible to per-user signing
Allow sender delegation
  Outsourcing
Low development, deployment, use costs
  Avoid large PKI, new Internet services
  No trusted third parties (except DNS)

## Slide 35: DKIM: Idea
Msg header authentication
  DNS identifiers
  Public keys in DNS
End-to-end
  Between origin/receiver
  administrative domains.
  Not path-based
※ Digital signatures

## Slide 36: DKIM: Technical High-points
Signs body and selected parts of header
Signature transmitted in DKIM-Signature header
Public key stored in DNS
  In _domainkey subdomain
  New RR type, fall back to TXT
Namespace divided using selectors
  Allows multiple keys for aging, delegation, etc.
Sender Signing Policy lookup for unsigned or improperly signed mail

## Slide 37: DKIM – Signature header (1/5)
v= Version
a= Hash/signing algorithm
q= Algorithm for getting public key
d= Signing domain
i= Signing identity
s= Selector
c= Canonicalization algorithm
t= Signing time (seconds since 1/1/1970)
x= Expiration time
h= List of headers included in signature; dkim-signature is implied
b= The signature itself
bh= Body hash
Notes: 1. 演算法，必須支持rsa-sha256，可選支持rsa-sha1。key size建議1024。王小雲老師在這裡貢獻不小。
2. 標準化(Canonicalization). 有的郵件服務器可能會少量修改文件內容，比如換行或者移除一些空格等等。因此DKIM定義了兩種標準化方法，simple和relaxed。simple 最簡單，就是一個字節也不能改，改了就錯。relaxed就是可以少量的修改一些空格等等。郵件頭和內容這兩部分的標準化可以選擇不同的方法，表示起來用 /隔開，比如simple/relaxed表示頭部用simple方式，內容用relaxed方式來標準化。
3. 過程。簽名是先對內容(body)部分hash，然後把這個body hash放在header裡面，再對頭部做簽名。頭部也不是所有字段都簽名的，只有一些常用的字段，或者比較有意義的，會被簽名。像Received和 Return-Path這樣的字段一般不被簽名。而From則必須被簽名。
# http://shawnma.xomud.com/tag/dkim/

## Slide 38: DKIM – Signature header (2/5)
Example:
DNS query will be made to:
Notes: • a= Hash/signing algorithm
• q= Algorithm for getting public key
• d= Signing domain
• i= Signing identity
• s= Selector
• c= Canonicalization algorithm
• t= Signing time (seconds since 1/1/1970)
• x= Expiration time
• h= List of headers included in signature; dkim-signature is implied
• b= The signature itself

## Slide 39: DKIM – Signature header (3/5)
DKIM-Signature: v=1; a=rsa-sha256; c=relaxed/relaxed;
d=yahoo.com.tw; s=s1024; t=1242033944;
bh=t3GnH+pN34KpMhlX59Eezm+9eCI68fU2hgid1Kscdrk=;
h=Message-ID:X-YMail-OSG:Received:X-Mailer:Date:From:Subject:
To:MIME-Version:Content-Type: Content-Transfer-Encoding;
b=emLg4QonGbqb3PhZIEoYfiQVDYMwcBBB6SAEW+RziBEhjxKS2O
UWmq5EpD1cxX+uz9MzJ4+fK4QRJZOtd0Y10c6Ce2J+V+C/RHnrjZ
3PF8kAhjqvT1GTTdohxivLGrMftg1xFGO//M7ML/fcI4UJL+XP1xhJMB
aHlHMGhE1sdGQ=
DomainKey-Signature: a=rsa-sha1; q=dns; c=nofws; s=s1024;
d=yahoo.com.tw; h=Message-ID:X-YMail-OSG:Received:X-Mailer:
Date:From:Subject:To:MIME-Version:Content-Type:Content-
Transfer-Encoding;
b=DlAhpuGID5ozcL77Ozm5doCQsxHSWaYHULW2hWAb3heXwewHga
mqO+McEcSIplcB1JXTIBka7BR6HvbSPWX/XiMrVAjvb6zeRWiXSBWdt
xIMpQhjJiBdzC8Y1BPCsdv2UwMgxOmR6i51BTIl+GDWFIKSgm5ky/
zU+ZsdwIhlss=;
Example: Signature of Yahoo Mail

## Slide 40: DKIM – Signature header (4/5)
DKIM-Signature: v=1; a=rsa-sha256; c=relaxed/relaxed; d=gmail.com;
s=gamma; h=domainkey-signature:mime-version:date:message-id:
subject:from:to:content-type;
bh=o8h0LUwAIau52hau5ntEJaPU6qQn7rkIboJwbgnuNgc=;
b=DxuMYeFtjXIt5eltj2MlzIXuOLA1y6f94+imgSKexX7EvhGMGUe82+4v
78Vrpm5xmkNKp2xHsjvESpyWEAyt22ZKEV4OHClyqWPuabpwas0UD
tV9KEwf9K663sCvrtoi9IpUQDPjP+aqC+po7tuLRiWfHYMETt5NpQfoWD
pmoXw=
DomainKey-Signature: a=rsa-sha1; c=nofws; d=gmail.com; s=gamma;
h=mime-version:date:message-id:subject:from:to:content-type;
b=T2N/3v39iaiL3tWBKoZadVYr5BsotqTIKe7QL3oEy1e+2OiUCIbLGepx
I7YXJ0Wt3MLx3ZcnkdNlGhrCWqXw7aV4gWw7GCsey2qZnakBTQ/BiH3
TyrD3vdaDB8KJU0jC3Q4uE+Y2jQalXC60wsJtCByCpdXq0VVorgpLCJg4
TnM=
Example: Signature of Google Mail

## Slide 41: DKIM DNS Records (1/2)
Related DNS Records (RFC 4870)
  t=y\; o=~\; n=…\;
nasa [/home/liuyh] -liuyh- dig _domainkey.yahoo.com txt
_domainkey.yahoo.com. 7160 IN TXT "t=y\; o=~\; n=http://antispam.yahoo.com/domainkeys"
nasa [/home/liuyh] -liuyh- dig _domainkey.cs.nctu.edu.tw txt
;; ANSWER SECTION:
_domainkey.cs.nctu.edu.tw. 3600 IN TXT "t=y\; o=~"
Notes: t=y test mode
o= policy. “=“ means this domain signs all mail, “~” means this domain may sign email (default)
n= nodes

## Slide 42: DKIM DNS Records (2/2)
Related DNS Records (RFC 4871)
  v=DKIM1\; k=rsa\; p=…\; n=…\;
  https://www.dnswatch.info/dkim/create-dns-record
nasa [/home/liuyh] -liuyh- dig s1024._domainkey.yahoo.com.tw txt
;; ANSWER SECTION:
s1024._domainkey.yahoo.com.tw. 1446 IN TXT "k=rsa\; t=y\; p=MIGfMA0GCSqGSIb3DQEBAQUAA4GNADCBiQKBgQDrEee0Ri4Juz+QfiWYui/E9UGSXau/2P8LjnTD8V4Unn+2FAZVGE3kL23bzeoULYv4PeleB3gfm" "JiDJOKU3Ns5L4KJAUUHjFwDebt0NP+sBK0VKeTATL2Yr/S3bT/xhy+1xtj4RkdV7fVxTn56Lb4udUnwuxK4V5b5PdOKj/+XcwIDAQAB\; n=A 1024 bit key\;“
nasa [/home/liuyh] -liuyh- dig gamma._domainkey.gmail.com txt
;; ANSWER SECTION:
gamma._domainkey.gmail.com. 300 IN TXT "k=rsa\; p=MIGfMA0GCSqGSIb3DQEBAQUAA4GNADCBiQKBgQDIhyR3oItOy22ZOaBrIVe9m/iME3RqOJeasANSpg2YTHTYV+Xtp4xwf5gTjCmHQEMOs0qYu0FYiNQPQogJ2t0Mfx9zNu06rfRBDjiIU9tpx2T+NGlWZ8qhbiLo5By8apJavLyqTLavyPSrvsx0B3YzC63T4Age2CDqZYA+OwSMWQIDAQAB"
Notes: t=y means test mode
s= service
n= note

## Slide 43: DKIM Signature Verification
Return-Path: <liuyh@cs.nctu.edu.tw>
Received-SPF: pass (google.com: domain of liuyh@cs.nctu.edu.tw designates 140.113.235.130 as permitted sender) client-ip=140.113.235.130;
Authentication-Results: mx.google.com; spf=pass (google.com: domain of liuyh@cs.nctu.edu.tw designates 140.113.235.130 as permitted sender) smtp.mail=liuyh@cs.nctu.edu.tw; dkim=pass (test mode) header.i=@cs.nctu.edu.tw
DKIM-Signature: v=1; a=rsa-sha1; c=relaxed; d=cs.nctu.edu.tw; h=date
:from:to:subject:message-id:mime-version:content-type
:content-transfer-encoding; s=rsa1024; bh=dOkD3r2GlhQkgTyMex5QXf
CG2H8=; b=U4thmEZOIV9Z7X4D4gdCM75rb23NtkNBooJr/qC2IMWlbKXBDfx27V
jG8pO0WYcKi9szdO0lZyQXBPh9RkqqOmd3w1sB8srTXOEifDcp0BrTo0tuyV9+R6
gwoWl2mi4HyQFMlqboRATLWkzqP38GGbESaDvucU6vbUPDjD3C6as=
DomainKey-Signature: a=rsa-sha1; c=nofws; d=cs.nctu.edu.tw; h=date:from
:to:subject:message-id:mime-version:content-type
:content-transfer-encoding; q=dns; s=rsa1024; b=YdHrlRhgxtafCn6h
Yuidyut1gsgDDKeqEfatQQZgyZ5aqD1dOF599RNa85w9Aisd+9gGese3YdHyBXh5
7X3fJNpGQTvgXr69rr8/zBW8FGknW/LfIR1uA0uEtyH3YDqpCMOmsW5/nVl87Lk7
T7nW4sFgbeeK3RRXUumz9JNQtLs=
Date: Mon, 21 May 2012 19:36:31 +0800
From: Yung-Hsiang Liu <liuyh@cs.nctu.edu.tw>
Subject: uwhefuwef
Message-ID: <20120521113631.GH87872@bsd5.cs.nctu.edu.tw>
test for dkim check

## Slide 44: DMARC
Domain-based Message Authentication, Reporting & Conformance
  An email authentication, policy, and reporting protocol
  It builds on SPF and DKIM protocols to provide greater assurance on the identity of the sender of a message
  Provides feedback data to Domain Owners
  Allow for blocking of unauthorized email
  Policies are published as TXT record of DNS Service _dmarc.example.com
https://dmarc.org

## Slide 45: DMARC – The Email Authentication Process
DMARC is designed to fit into an organization’s existing inbound email authentication process

## Slide 46: DMARC Record Syntax – Tag (1/3)
v=<version>
  <version>: DMARC1
  Mandatory. This must be the first supplied tag=value within the dmarc specific text and, while DMARC tag=value pairs are not case sensitive, this one must have the explicit upper-case value DMARC1
p=<policy>
  <policy>: none, quarantine, reject
    none: Monitoring, no impact on mail flows
    quarantine: Deliver to spam folder
    reject: Block mail that fails the DMARC check
  Mandatory and must be the second tag=value pair. Defines the policy the sending MTA advises the receiving MTA to follow

## Slide 47: DMARC Record Syntax – Tag (2/3)
sp=<sub-domain policy>
  <sub-domain policy>: none, quarantine, reject
  Optional. If the following DMARC RR is present:
Then failed mail from user@example.com would be rejected but
  mail from user@a.example.com or user@b.a.example.com or
  user@anything.example.com would be quarantined
$ORIGIN example.com.
...
_dmarc IN TXT "v=DMARC1;p=reject;sp=quarantine"

## Slide 48: DMARC Record Syntax – Tag (3/3)
rua=<@mail>
  <@mail>: Optional. A comma delimited list of URI(s) to which aggregate mail reports should be sent
ruf=<@mail>
  <@mail>: Optional. A comma delimited list of URI(s) to which detailed failure reports should be sent
pct=<percent>
  <percent>: Number from 0 to 100
  Optional. Defines the percentage of mail to which the DMARC policy applies

## Slide 49: Handling Malicious Mail in Postfix

## Slide 50: Postfix Anti – Spam configuration
The SMTP Conversation
  info@ora.com  smtp.example.com  kdent@example.com

## Slide 51: Postfix Anti – Spam configuration – Client Detection Rules (1)
Four rules in relative detection position
  Rules and their default values
    smtpd_client_restrictions =
      smtpd_helo_required = yes
    smtpd_helo_restrictions =
    smtpd_sender_restrictions =
    smtpd_recipient_restrictions =
    permit_mynetworks, reject_unauth_destination
  Each restriction check result can be:
    OK (Accept in this restriction)
    REJECT (Reject immediately without further check)
    DUNNO (do next check)
  Other options
    disable_vrfy_command = yes

## Slide 52: Postfix Anti – Spam configuration – Client Detection Rules (2)
DNSBL/WL
  smtpd_client_restrictions
Greylisting
  smtpd_recipient_restrictions
SPF
  smtpd_recipient_restrictions

## Slide 53: Postfix Anti – Spam configuration – Client Detection Rules (3)
Access maps – access(5)
  List of IP addresses, hostnames, email addresses
  Can be used in:
  smtpd_client_restrictions = check_client_access hash:/usr/local/etc/postfix/access
  smtpd_helo_restrictions = check_helo_access hash:/usr/local/etc/postfix/helohost
  smtpd_sender_restrictions = check_sender_access hash:/usr/local/etc/postfix/sender_access
  smtpd_recipient_restrictions = check_recipient_access hash:/usr/local/etc/postfix/rcpt_access
  Actions
    OK, REJECT, DUNNO
    FILTER (redirect to content filter)
    HOLD (put in hold queue)
    DISCARD (report success to client but drop)
    4xx message or 5xx message

## Slide 54: Postfix Anti – Spam configuration – Client Detection Rules (4)
  Example of access maps
    check_client_access hash:/etc/access
    nctu.edu.tw OK
    127.0.0.1 OK
    61.30.6.207 REJECT
    /\.dynamic\./ REJECT (regexp:)
    check_helo access hash:/postfix/helohost
    greatdeals.example.com REJECT
    oreillynet.com OK
    check_sender_access hash:/usr/local/etc/postfix/sender_access
    sales@viagra.com 553 Please contact +886-3-5712121-54707.
    viagra.com 553 Invalid MAIL FROM
    .viagra.com 553 Invalid MAIL FROM
    manager@ 553 Invalid MAIL FROM
    check_recipient_access hash:/usr/local/etc/postfix/recipient_access
    bin@cs.nctu.edu.tw 553 Invalid RCPT TO command
    ftp@cs.nctu.edu.tw 553 Invalid RCPT TO command
    man@cs.nctu.edu.tw 553 Invalid RCPT TO command

## Slide 55: Postfix Anti – Spam configuration – Client Detection Rules (5)
Special client-checking restrictions
  permit_auth_destination
    Mostly used in “smtpd_recipient_restrictions”
    Permit request if destination address matches:
      The postfix system’s final destination setting
        mydestination, inet_interfaces, vitual_alias_domains, virtual_mailbox_domains
      The postfix system’s relay domain
        relay_domains
    Found  OK, UnFound  DUNNO
  reject_unauth_destination
    Opposite to permit_auth_destination
    Found  REJECT, UnFound  DUNNO
  permit_mynetworks
    Allow a request if client IP match any address in “mynetworks”
      Usually used in smtpd_recipient_restrictions

## Slide 56: Postfix Anti – Spam configuration – Client Detection Rules (6)
Strict syntax restrictions
  Restrictions that does not conform to RFC
  reject_invalid_helo_hostname
    Reject hostname with bad syntax
  reject_non_fqdn_helo_hostname
    Reject hostname not in FQDN format
  reject_non_fqdn_sender
    For “MAIL FROM” command
  reject_non_fqdn_recipient
    For “RCPT TO” command

## Slide 57: Postfix Anti – Spam configuration – Client Detection Rules (7)
DNS restrictions
  Make sure that clients and email envelope addresses have valid DNS information
  reject_unknown_client_hostname
    Reject if the DNS records related to the client IP unreasonable
  reject_unknown_helo_hostname
    Reject if EHLO hostname has no DNS MX or A record
  reject_unknown_sender_domain
    Reject if MAIL FROM domain name has no DNS MX or A record
  reject_unknown_recipient_domain
    Reject if RCPT TO domain name has no DNS MX or A record

## Slide 58: Postfix Anti – Spam configuration – Client Detection Rules (8)
Real-time blacklists
  Check with DNSxL services
  permit_dnswl_client list.dnswl.org
    http://www.dnswl.org/
  reject_rbl_client domain.tld[=d.d.d.d]
    Reject if client IP is detect in DNSBL
  reject_rhsbl_client domain.tld[=d.d.d.d]
    Reject if client hostname has an A record under specified domain
  reject_rhsbl_sender domain.tld[=d.d.d.d]
    Reject if sender domain in address has an A record under specified domain
  smtpd_client_restrictions = hash:/etc/access, reject_rbl_client relays.ordb.org
  smtpd_sender_restrictions =
  hash:/usr/local/etc/postfix/sender_access,
  reject_rhsbl_sender dns.rfc-ignorant.org

## Slide 59: Postfix Anti – Spam configuration – Client Detection Rules (9)
Policy Service
  Postfix SMTP server sends in a delegated SMTPD access policy request to one special service (policy service).
  Policy service replies actions allowed in Postfix SMTPD access table.
  Usage:
    check_policy_service servicename
  Example: Greylisting (Using Postgrey)
    mail/postgrey
      /usr/local/etc/postfix/postgrey_whitelist_clients
      /usr/local/etc/postfix/postgrey_whitelist_recipients
    postgrey daemon runs on port 10023
    In main.cf
      smtpd_recipient_restrictions = …, reject_unauth_destination, check_policy_service inet:127.0.0.1:10023

## Slide 60: Postfix Anti – Spam configuration – Client Detection Rules (10)
  Example: SPF Checking (Using postfix-policyd-spf-perl)
    mail/postfix-policyd-spf-perl
      /usr/local/etc/postfix/postgrey_whitelist_clients
      /usr/local/etc/postfix/postgrey_whitelist_recipients
    SPF policy service daemon runs on a Unix domain socket
    In master.cf
    In main.cf
      smtpd_recipient_restrictions = …, reject_unauth_destination, check_policy_service unix:private/policy-spf
      spf-policy_time_limit = 3600
policyd-spf unix - n n - 0 spawn user=nobody argv=/usr/local/libexec/postfix-policyd-spf-perl

## Slide 61: Postfix Anti – Spam configuration – Client Detection Rules (11)
smtpd_client_restrictions
  check_client_access
  reject_unknown_client_hostname
  permit_mynetworks
  reject_rbl_client
  reject_rhsbl_client
smtpd_helo_restrictions
  check_helo_access
  reject_invalid_helo_hostname
  reject_unknown_helo_hostname
  reject_non_fqdn_helo_hostname
smtpd_sender_restrictions
  check_sender_access
  reject_unknown_sender_domain
  reject_rhsbl_sender
smtpd_recipient_restrictions
  check_recipient_access
  permit_auth_destination
  reject_unauth_destination
  reject_unknown_recipient_domain
  reject_non_fqdn_recipient
  check_policy_service

## Slide 62: Postfix Anti – Spam configuration – Content Inspection
before queue, built-in, light-weight
  header_checks, body_checks
after queue, external, heavy-weight
  Use smtp, pipe, etc. to inject mail to filters
    content_filter
  Accept: Re-inject mail back into Postfix
  Reject: Discard mail / Reject mail
before queue, external, medium-weight
  Method 1: SMTP proxy (smtp)
    smtpd_proxy_filter
  Method 2: Sendmail Milter (milter protocol)
    SMTP-only: Invoked by smtpd(8), for mail arriving via smtpd(8) server
      smtpd_milters, milter_*
    non-SMTP: Invoked by cleanup(8), for mail arriving via sendmail(1), i.e. local mail
      non_smtpd_milters, milter_*
Pros and cons
  http://www.postfix.org/documentation.html “Content inspection” Section

## Slide 63: Postfix Anti – Spam configuration – Content – Checking rules (1)
4+ rules – header_checks(5)
  header_checks
    Check for message headers
  mime_header_checks
    Check for MIME headers
  nested_header_checks
    Check for attached message headers
  body_check
    Check for message body
All rules use lookup tables
  Ex:
    header_checks = regexp:/usr/local/etc/postfix/header_checks
    body_checks = pcre:/usr/local/etc/postfix/body_checks

## Slide 64: Postfix Anti – Spam configuration – Content – Checking rules (2)
Content-checking lookup table
  Regular_Expression Action
Actions
  REJECT message
  WARN message
    Log a “warning:” record, for debugging
  IGNORE
    Delete matched line of headers or body
  HOLD message
    Stay there until the administrator intervenes
  DISCARD message
    Claim successful delivery but silently discard
  FILTER message
    Send message through a separate content filter

## Slide 65: Postfix Anti – Spam configuration – Content – Checking rules (3)
Example of header check
  header_checks = regexp:/usr/local/etc/postfix/header_checks
  In /usr/local/etc/postfix/header_checks
  /take advantage now/ REJECT
  /repair your credit/ REJECT
Example of body check
  body_checks = regexp:/usr/local/etc/postfix/body_checks
  In /usr/local/etc/postfix/body_checks
  /lowest rates.*\!/ REJECT
  /[:alpha:]<!--.*-->[:alpha:]/ REJECT

## Slide 66: External Filters (After-queue) – (1)
After-queue filters can be done on
  MTA
  MDA
  MUA
  ※ Combination of MTA and MUA
    Adding some extra headers or modifying subject in MTA, and filtering in MUA.
Types of after-queue external filters
  Command-based filtering
    New process is started for every message
    Accept message from STDIN
  Daemon-based filtering
    Stay resident
    Accept message via SMTP or LMTP

## Slide 67: External Filters (After-queue) – (2)
  https://www.postfix.org/FILTER_README.html

## Slide 68: MDA Filter: Procmail (1)
Install Procmail (port or package)
Enable Procmail in Postfix
  In main.cf
Create configuration file
  Create /usr/local/etc/procmailrc
Create log files
  touch /var/log/procmail.log
Create directories (optional)
  mkdir -p /tmp/trash
mailbox_command = /usr/local/bin/procmail
VERBOSE=off
LOGFILE=/var/log/procmail.log
:0b
* ^Subject:.*GGWP.*
/dev/null
:0b
* ^Subject:.*LOL.*
/tmp/trash
procmailrc

## Slide 69: MDA Filter: Procmail (2-1) - Filter Chinese Text
Encoding problem
  We need to set two types of encoded Chinese text
  Base64 and Quote-Printable
Tool: mmencode (port or package)
Generate encoded text
  Filter “減肥”
  Generate Base64 code
  Generate QP code
> echo -n "減肥" | mmencode
5rib6IKl
> echo -n "減肥" | mmencode -q
=E6=B8=9B=E8=82=A5=

## Slide 70
Write two rules to filter Chinese text
Log file
# Base64
:0b
* ^Subject:.*5rib6IKl.*
/dev/null
# Quote-Printable
:0b
* ^Subject:.*=E6=B8=9B=E8=82=A5=.*
/dev/null
From lctseng@nasa.lctseng.nctucs.net Wed Mar 9 12:14:46 2016
Subject: =?UTF-8?B?5rib6IKl?=
Folder: /dev/null 1
MDA Filter: Procmail (2-2) - Filter Chinese Text

## Slide 71: Command-Based Filtering (1)
Usage
  Postfix delivers message to this filter via “pipe” mailer
  Program that accepts content on its STDIN
  Program gives the filtered message back to Postfix using the “sendmail” command (with same queue ID)

## Slide 72: Command-Based Filtering (2)
Configuration
  Prepare your filter program (/usr/local/bin/simple_filt)
  Modify master.cf
#==========================================================================
# service type private unpriv chroot wakeup maxproc command + args
#==========================================================================
filter unix - n n - - pipe
flags=Rq user=filter argv=/usr/local/bin/simple_filt -f ${sender} - -${recipient}
smtpd inet n - n - - smtpd
-o content_filter=filter:

## Slide 73: Daemon-Based Filtering (1)
Usage
  Message is passed back and forth between Postfix and filtering daemon via SMTP or LMTP

## Slide 74: Daemon-Based Filtering (2) - amavisd-new
Primary daemon: amavisd-new
  Cooperate with other programs
  ClamAV (anti-virus), SpamAssassin (anti-spam)
Configuration for amavisd
  Install and configure your content filter
    security/amavisd-new (port or package)
    Modify amavisd.conf to send message back
  Edit /etc/rc.conf
  Edit main.cf to let postfix use filtering daemon
$forward_method = 'smtp:127.0.0.1:10025';
amavisd_enable="YES"
content_filter = smtp-amavis:[127.0.0.1]:10024

## Slide 75: Daemon-Based Filtering (3) - amavisd-new
Configuration
  Edit master.cf to add two additional services
smtp-amavis unix - - n - 10 smtp
-o smtp_data_done_timeout=1200s
-o smtp_never_send_ehlo=yes
-o notify_classes=protocol,resource,software
127.0.0.1:10025 inet n - n - - smtpd
-o content_filter=
-o mynetworks=127.0.0.0/8
-o local_recipient_maps=
-o notify_classes=protocol,resource,software
-o myhostname=localhost
-o smtpd_client_restrictions=
-o smtpd_sender_restrictions=
-o smtpd_recipient_restrictions=permit_mynetworks,reject
-o smtpd_tls_security_level=

## Slide 76: Daemon-Based Filtering (4) - amavisd-new
Now, your amavisd-new is ready
  With SpamAssassin installed
  Run “sa-update” to update the SpamAssassin rules
  Edit SpamAssassin configuration in amavisd.conf
    E.g. Change spam detect level
$sa_tag2_level_deflt = 3.0;

## Slide 77: Daemon-Based Filtering (5) - amavisd-new
The mail source in SPAM-detected mail
Received: from demo1.nasa.lctseng.nctucs.net (localhost [127.0.0.1])
by localhost (Postfix) with ESMTP id 1A945274
for <lctseng@nasa.lctseng.nctucs.net>; Wed, 9 Mar 2016 14:14:39 +0800 (CST)
X-Virus-Scanned: amavisd-new at nasa.lctseng.ncatucs.net
X-Spam-Flag: YES
X-Spam-Score: 4.85
X-Spam-Level: ****
X-Spam-Status: Yes, score=4.85 tagged_above=2 required=3
tests=[FREEMAIL_ENVFROM_END_DIGIT=0.25, FREEMAIL_FROM=0.001,
HTML_FONT_LOW_CONTRAST=0.001, HTML_MESSAGE=0.001,
RCVD_IN_DNSWL_LOW=-0.7, RCVD_IN_MSPIKE_H3=-0.01,
RCVD_IN_MSPIKE_WL=-0.01, T_REMOTE_IMAGE=0.01, URIBL_ABUSE_SURBL=1.948,
URIBL_BLACK=1.7, URIBL_WS_SURBL=1.659] autolearn=no autolearn_force=no
Authentication-Results: demo1.nasa.lctseng.nctucs.net (amavisd-new);
dkim=pass (2048-bit key) header.d=gmail.com
Received: from demo1.nasa.lctseng.nctucs.net ([127.0.0.1])
by demo1.nasa.lctseng.nctucs.net (demo1.nasa.lctseng.nctucs.net [127.0.0.1]) (amavisd-new, port 10024)
with SMTP id CjRyliYl5l6x for <lctseng@nasa.lctseng.nctucs.net>;
Wed, 9 Mar 2016 14:14:38 +0800 (CST)

## Slide 78: Daemon-Based Filtering (6) - amavisd-new+ ClamAV
amavisd-new supports lots of anti-virus scanner
Anti-virus with ClamAV
  Install security/clamav (port or package)
  Edit /etc/rc.conf
  Update virus database
    Run “freshclam”
  Specify to use clamav in amavisd.conf
clamav_clamd_enable="YES"
@av_scanners = (
['ClamAV-clamd',
\&ask_daemon, ["CONTSCAN {}\n", "/var/run/clamav/clamd.sock"],
qr/\bOK$/m, qr/\bFOUND$/m,
qr/^.*?: (?!Infected Archive)(.*) FOUND$/m ],
);

## Slide 79: Daemon-Based Filtering (7) - amavisd-new+ ClamAV
Set alias for “virusalert” user
  When there is an infected mail, it will send a notification to this user
  Alias to “root” or “postmaster”
Start ClamAV and restart amavisd-new
  service clamav-clamd start
  service amavisd restart
Send a test virus by EICAR organization
  Plain text
  Reference: https://en.wikipedia.org/wiki/EICAR_test_file
X5O!P%@AP[4\PZX54(P^)7CC)7}$EICAR-STANDARD-ANTIVIRUS-TEST-FILE!$H+H*

## Slide 80: Daemon-Based Filtering (8) - amavisd-new+ ClamAV
Result of sending EICAR test mail

## Slide 81: External Filters (Before-queue) – (1)
Types of before-queue external filters
  SMTP proxy (smtp)
    smtpd_proxy_filter
  From after-queue to before-queue (Software support)
    content_filter  smtpd_proxy_filter
  http://www.postfix.org/SMTPD_PROXY_README.html

## Slide 82: External Filters (Before-queue) – (2)
Types of before-queue external filters
  Sendmail Milter (milter protocol)
    SMTP-only: Invoked by smtpd(8), for mail arriving via smtpd(8) server
      smtpd_milters, milter_*
    non-SMTP: Invoked by cleanup(8), for mail arriving via sendmail(1), i.e. local mail
      non_smtpd_milters, milter_*
https://www.postfix.org/MILTER_README.html

## Slide 83: Appendix
Postfix Postscreen
Rspamd

## Slide 84: postscreen – Postfix zombie blocker
Postscreen (Postfix ≥ 2.8)
  Provide additional protection against mail server overload
  Handle multiple inbound SMTP connections in one process
  Decide which clients may talk to the Postfix SMTP server process
How it works?
  Maintain a temporary whitelist for clients passing its tests
  Allow whitelisted clients to skip tests
CAUTION
  Not be used on SMTP ports that receive mail from MUAs
  postscreen is used on port 25
  MUAs submit mail via the submission service (port 587)
    Separate IMG/OMG: MX settings
  http://www.postfix.org/POSTSCREEN_README.html

## Slide 85: postscreen – Basic idea
Most mails are spam
  Spend most resources not receiving mail
Mail challenge: Keep zombies away
  Make an is-it-a-zombie decision
  Whitelist while deciding a client not-a-zombie to avoid further delay
Zombies’ challenge:
  Only a limited amount of time to deliver spam before being blacklisted
  To speed up
    Speak before their turn
    Ignore response from SMTP servers
To recognize zombies
  Determine if the remote SMTP client IP is blacklisted
  Look for protocol compromises

## Slide 86: postscreen – General operation
postscreen
  Involve a number of tests
Some tests introduce a delay of a few seconds
  Maintain a temporary whitelist for clients passing its tests
  Minimize its impact on legitimate email traffic
Default
  Hand off all connections to the SMTP server after logging
  Useful for non-destructive testing
Typical production setting
  Reject mail from clients failing one or more tests
  Log helo, sender, and recipient information

## Slide 87: postscreen – Quick tests
Query local blacklists/whitelists
  Permanent whitelist/blacklist test
    postscreen_access_list = permit_mynetworks, cidr:postscreen_access.cidr
    In postscreen_access.cidr (first-matching) 192.168.0.1 permit / dunno 192.168.0.0/16 reject
    WHITELISTED [address]:port BLACKLISTED [address]:port
  Temporary whitelist test
    PASS OLD [address]:port
  MX policy test
    postscreen_whitelist_interfaces = !168.100.189.8 static:all
    CONNECT from [address]:port to [168.100.189.8]:25 WHITELIST VETO [address]:port
Notes: postscreen_blacklist_action

## Slide 88: postscreen – Tests before greeting – (1)
The SMTP server should speak before the client
  A short delay before "220 …" server greeting
    For DNSWL/BL lookup results to arrive
    postscreen_greet_wait = ${stress?2}${stress:6}s
Pregreet test
  Detect zombies that speak before their turn
  postscreen_greet_banner = $smtpd_banner
    "220-text …" vs. "220 text …“
    Disable the teaser banner
      postscreen_greet_banner =
  PREGREET count after time from [address]:port text...

## Slide 89: postscreen – Tests before greeting – (2)
DNSWL/BL test
  postscreen_dnsbl_sites = highqualityblacklist.example.com*2 lowerqualityblacklist.example.net list.dnswl.org*-5 example.com=127.0.0.4
  postscreen_dnsbl_threshold = 1
    Determine when postscreen_greet_wait time has elapsed
  postscreen_dnsbl_reply_map = texthash:dnsbl_reply
    In dnsbl_reply secret.zen.spamhaus.org zen.spamhaus.org
  DNSBL rank count for [address]:port
  Wietse needed new material for a LISA conference presentation in November 2010, so he added support for DNSBL weights and filters in August

## Slide 90: postscreen – Tests fail before greeting
Actions
  ignore (default)
  enforce
    Allow other tests to complete, reply 550, and log helo/sender/recipient
  drop
    Reply 521 immediately
postscreen_*_action
  postscreen_blacklist_action
    Match permanent blacklist
  postscreen_greet_action
    Fail pregreet test
  postscreen_dnsbl_action
    DNSBL score is equal to or greater than the threshold

## Slide 91: postscreen – Workflow before SMTP
Accept connection
Static W/B list DNS W/B list Pregreet test Primary MX test
Reject or defer mail (and log from, to, client, helo)
Add client to temp whitelist
Hand-off to real SMTP server
No
Yes
Pass
Fail
Close connection
Is client in temp whitelist
Fast path: ~0.1 ms
Slow path: up to ~6 seconds
Dummy SMTP and TLS engine

## Slide 92: postscreen – Multi-layer defense
Layer 1
  Block connections from zombies and other spambots
  Single process
  90% of all spams
Layer 2
  Complex SMTP access checks
  Postfix SMTP server, policy daemons, Milter applications
Layer 3
  Light-weight content inspection
  header_checks, body_checks
Layer 4
  Heavy-weight content inspection with external content filters

## Slide 93: postscreen – Tests after greeting – (1)
"Deep protocol" tests
  Use an SMTP protocol engine built into postscreen
  When a good client passes the tests
    Add the client to the temporary whitelist
    CAN*NOT* hand off the live connection to the SMTP server
    Reply 4xx status
  Built-in SMTP engine does *NOT* implement
    AUTH
      May be added in the feature
      (Workaround) Not enable tests after greeting
      (Workaround) End-user should connect directly to the submission service
    XCLIENT
    XFORWARD

## Slide 94: postscreen – Tests after greeting – (2)
Command pipelining test
  Not announce support for ESMTP command pipelining
    postscreen_pipelining_enable
    postscreen_pipelining_action = enforce
Non-SMTP command test
  Block clients sending commands in postscreen_forbidden_commands
    postscreen_non_smtp_command_enable
    postscreen_non_smtp_command_action = drop
Bare newline test
  Block clients whose sending lines ended with ‘\n’ instead of ‘\r\n’
    postscreen_bare_newline_enable
    postscreen_bare_newline_action = ignore

## Slide 95: postscreen – Workflow before/after SMTP
Accept connection
Local W/B list DNS W/B list Pregreet test Primary MX test
Reject or defer mail (and log from, to, client, helo)
Add client to temp whitelist
Hand-off to real SMTP server
No
Yes
Pass
Fail
Close connection
Is client in temp whitelist
Pipelining, non-SMTP command, bare newline
Pass
Fail
Defer
Dummy SMTP and TLS engine

## Slide 96: postscreen – Other errors
Too many connections
  postscreen_client_connection_count_limit = $smtpd_client_connection_count_limit = 50
    NOQUEUE: reject: CONNECT from [address]:port: too many connections
  postscreen_pre_queue_limit = $default_process_limit = 100
    NOQUEUE: reject: CONNECT from [address]:port: all server ports busy
Others
  HANGUP after time from [address]:port in test name
  COMMAND TIME/COUNT/LENGTH LIMIT from [address]:port

## Slide 97: postscreen – When all tests succeed
Create a temporary whitelist entry
  Controlled with the postscreen_*_ttl parameters
  PASS NEW [address]:port
No "deep protocol tests"
  Hand off the "live" connection to the SMTP server
  The client can continue as if postscreen never existed
When using "deep protocol tests"
  Reply 4xx
  Log helo, sender, and recipient
  Mitigate the impact by giving long TTL

## Slide 98: postscreen – Turning on – (1)
In master.cf
  Original smtp: smtpd  postscreen
  New smtpd: smtpd
    Handle SMTP connections handed off by postscreen
  New dnsblog: dnsblog
    DNSBL/WL lookups
  New tlsproxy: tlsproxy
    Support STARTTLS
    The implementation led to the discovery of a new class of vulnerabilities
  New submission: smtpd
    Listen on 587, and wait for MUAs
#smtp inet n - n - - smtpd
smtp inet n - n - 1 postscreen
smtpd pass - - n - - smtpd
dnsblog unix - - n - 0 dnsblog
#tlsproxy unix - - n - 0 tlsproxy
#submission inet n - n - - smtpd

## Slide 99: postscreen – Turning on – (2)
Blocking mail with postscreen
  postscreen_blacklist_action
  postscreen_greet_action
  postscreen_dnsbl_action
  For testing postscreen functionality
    soft_bounce=yes
    In master.cf
      -o soft_bounce=yes

## Slide 100: Rspamd
Rapid spam filtering system (https://rspamd.com)
  https://github.com/rspamd/rspamd
  https://rspamd.com/features.html
  https://rspamd.com/comparison.html
  https://rspamd.com/doc/integration.html
  https://www.rspamd.com/doc/modules/antivirus.html
#smtpd_milters = unix:/var/lib/rspamd/milter.sock
# or for TCP socket
smtpd_milters = inet:localhost:11332
# skip mail without checks if something goes wrong
milter_default_action = accept
# 6 is the default milter protocol version;
# prior to Postfix 2.6 the default protocol was 2.
# milter_protocol = 6